## Slide 1: ARC Closing Report
Date: 2025-03-14
Authors:

## Slide 2: Abstract
This document is the closing report for ARC SC,
March 2025 Session

## Slide 3: Annex G update/replacement
Continued discssion on the proposal for Annex G replacement: 11-23/0880r7, 11-25/0193r4, 11-25/0488r0
This is uncovering mis-alignment among experts on key concepts:
  “Frame exchange sequence” (and its relationship to/meaning for other behaviors like power save/doze, off-channel scanning, etc.)
  Relation of frame exchange sequence to medium protection (NAV, etc.)
  The definition and extent of an occurrence of Wireless Medium
  Relation of wireless medium to beamforming, sectorization, MU operation, etc.
Straw Polls didn’t help (much controversy on the questions)
Especially tricky as MLO, and now TGbn concepts are added/considered
Will continue discussion in May. Allocating 2 meeting slots worked well – will do that again, to try to sort out these terms and concepts.

## Slide 4: Std 802 update impacts on 802.11
Reviewed 11-25/0150r4 discussion document
      Agreed direction, ready for specific text proposals:
        EPD and LPD terms are going away – we need to update 802.11 to align
        MAC address ordering discussion, and 802.11 assumptions
        https://mentor.ieee.org/802.1/dcn/24/1-24-0034-00-Mntg-proposal-to-revise-bit-ordering-material-in-p802revc-d2-0.docx
        Review 802.1AC mapping from ISS to 802.11 MAC SAP interface
        Any other changes to remove 802.2/LLC terms?
      Continue next session:
        802.11’s “Portal”, and mapping to/usage of IEEE Std 802 terminology
  Access Domains: “802 Access Domains”?
    Interconnection of Access Domains?
    In 802.11, Access Domain is BSS. Is that still the view, for 802.11be/MLD?
    Other 802s? 802.3 Multi-carrier fiber – 1 Access Domain, or many? We think it’s 1. But, there are multiple transmitters, in parallel.
  What if we make the DS a bridge (small ‘b’)?
Consider adding something about VLANs (just informational?) into 802.11? Relationship (if we talk about it) to security domains (e.g. Authenticator relationship)? VLAN-aware STAs? What about GLK/non-GLK STAs? (cf 11-08/0114r0)

## Slide 5: Other topics
IEEE Std 802 revision (no change since Jan):
  Received a report on the P802REV activities
    Approvals are completed. Going through publication editing.
WBA L4S (no change since Jan):
  No discussion this session.
  Per request from proponents, ARC is deferring for discussion in TGbn and perhaps REVmf. ARC will step in with any support needed by those groups.
Still pending:
  MLME-RESET, versus MLME-JOIN, MLME-START, MLME-SCAN and MLME-END
Agenda is here: 11-25/0222r5

## Slide 6: Plans
Next session/teleconference topics:
Continue EPD/LPD clean-up, other Std 802 alignment
Continue Annex G replacement
MLME clean-up
Teleconferences – None planned (may schedule with 10 days’ notice, depending on progress on reflector discussion on Annex G)
Three meeting slots requested in May