## Slide 1: UHR Sounding Feedback Extension
Date: 2025-04-11
Authors:

## Slide 2: Introduction
The UHR sounding operation have been defined in 802.11bn™/D0.2 for implementing DL coordinated beamforming transmission. UHR sounding operation provides a feedback mechanism that enable UHR STAs reporting cross-BSS Compressed Beamforming/CQI frames to the associated AP[1].
RSSI information is the significant parameter in implementing some operations(eg, TX power controlling in Co-SR, target AP selection in seamless roaming)
In this contribution, we discuss a mechanism to enable UHR STAs reporting RSSI to the associated AP by extending the UHR Sounding Feedback type.

## Slide 3: Observation: RSSI Measurement in Co-SR
RSSI information between each AP and non-AP STA is needed
  Each non-AP STA measure intra-BSS and cross-BSS RSSI of the signals from each AP
  AP requests non-AP STAs to report intra-BSS and cross-BSS RSSI
AP-1
AP-2
STA-1
Associated with AP-1
Intra-BSS RSSI measurement
Cross-BSS RSSI measurement
RSSI measurement sequence (from AP1)
Notes: Link Measurement Request frame

## Slide 4: Recap: UHR Sounding Procedure
UHR TB sequential NDP sounding procedure in UHR sounding operation[2]

## Slide 5: Proposal: RSSI Sounding Procedure
We propose reusing the UHR sequential NDP sounding procedure to obtain the RSSI info by extending the UHR sounding feedback type.
The sounding feedback type extension is indicated in the UHR NDP Announcement frame
The receiving STA shall send the feedback to the AP including the RSSI Indication info
AP-1
AP-2
STA-1
Associated with AP-1
UHR NDP Announcement
BFRP Trigger
SIFS
RSSI Info Feedback
SIFS
SIFS
EHT sounding
NDP
RSSI Info Feedback
UHR NDP Announcement
BFRP Trigger
SIFS
SIFS
SIFS
EHT sounding
NDP
Intra-BSS RSSI measurement
Cross-BSS RSSI measurement

## Slide 6: Design of UHR NDP Announcement Frame
Frame Control | Duration | RA | TA | Sounding Dialog Token | 1st User Info field | 2nd User Info field | STA1 Info | … | FCS
Define a indication for feedback type extension in UHR NDP Announcement frame.
  Define the reserved bit(B20) in the STA Info filed as the Feedback Type Extension
  A STA receiving the B20 set to 1 shall send the feedback including RSSI info
B0
AID11 | Partial BW Info | Reserved | Nc Index | Feedback Type And Ng | Disambiguation | Codebook Size | Reserved
B10
B11
B19
B20
B21
B24
B25
B26
B27
B28
B29
B31
Feedback Type Extension
UHR NDP Announcement frame format
Feedback type extension | Feedback Type And Ng |  | Codebook Size | Description
B20 | B25 | B26 | B28 | 
0 | 0 | 0 | 0 | SU
0 | 0 | 0 | 1 | SU
0 | 0 | 1 | 0 | SU
0 | 0 | 1 | 1 | SU
0 | 1 | 0 | 0 | MU
0 | 1 | 0 | 1 | MU
0 | 1 | 1 | 0 | CQI
0 | 1 | 1 | 1 | MU
1 | X | X | X | RSSI

## Slide 7
RSSI Info Feedback Design
Action frame format
Category | UHR/EHT Action | Action dependent Field
Valve | Meaning
0 | EHT Compressed Beamforming/CQI
1 | RSSI Info Feedback (eg, RCPI element )
2-255 | reserved
The RSSI info feedback is similar with the feedback operation in Co-BF
  RSSI info is reported in a Action frame (EHT Action/UHR Action frame)
  RSSI value can be indicated by reusing RCPI element
Element ID | Length | RCPI
1 | 1 | 1
RCPI element format
RCPI parameter | value
0 | Power ≤ – 110 dBm
1 | Power = – 109.5 dBm
2 | Power = – 109.0 dBm
… | …
220 | Power ≥ – 0 dBm
221–254 | Reserved
255 | Measurement not available

## Slide 8
Summary
In this contribution, we propose a mechanism to extend the feedback type in the UHR sounding operation for obtaining Cross-BSS RSSI info.
  The feedback type extension is indicated by a reserved bit in STA info subfield in the NDPA frame
  The RSSI info feedback can be indicated by reusing the RCPI element

## Slide 9: Straw poll 1
Do you agree adding the following text to the SFD:
  Define a mechanism for cross-BSS RSSI measurement in 11bn
    The measurement reuse the UHR sounding operation
    The RSSI info feedback is TBD
Y/N/A:

## Slide 10: References
[1] 802.11bn™/D0.2
[2] 11-24-1542-05-00bn-sounding-schemes-for-coordinated-beamforming