## Slide 1: Further Discussion on Co-BF
Date: 2025-04-13
Authors:

## Slide 2: Introduction
Multi-AP Coordinated Beamforming (Co-BF) has be defined in the 802.11bn™/D0.2 [1]
In general Co-BF scenarios, all receiving STAs are in the OBSS region. However, some receiving STAs may move to the edge of the OBSS region during the cross-BSS sounding procedure and send distorted CSI feedback to compute Co-BF steering matrices, which may induce unexpected inter-BSS interference.
In this contribution, we discuss portion CSI feedback operation in Co-BF procedure.

## Slide 3: Recap: UHR Co-BF Procedure
There shall be a frame-exchange before the Co-BF sounding between the two APs which will at-least serve the following goals:
  Unavailability/decline indication from the responding AP
    Used by responding AP to refuse participation in a COBF sounding process
  Exchange of sounding Nss capability of the STAs being sounded in the two BSSs
    The minimum sounding Nss capability of the participating STAs in each BSS will be exchanged
  Note: Design of the frames is TBD by MAC group
AP-1
AP-2
Co-BF Sounding
[Motion #306, [2]]
Sounding Nss capability exchange
Co-BF Transmission

## Slide 4: Recap: UHR Co-BF Sounding
UHR TB sequential NDP sounding sequence
AP-1
AP-2
STA-1
Associated with AP-1
UHR NDPA
EHT NDP
BFRP Trigger
SIFS
EHT Compressed Beamforming/CQI[2]
SIFS
SIFS
EHT NDPA
EHT NDP
BFRP Trigger
SIFS
EHT Compressed Beamforming/CQI
SIFS
SIFS
Cross-BSS UHR TB Sounding
EHT TB Sounding

## Slide 5: Case Consideration
During cross-BSS sounding procedure, a STA (eg, STA-31) addressed by a UHR NDP Announcement frame move to the edge of the OBSS and may
  Respond the CSI feedback (Low average SNR)
    Low average SNR may result in unexpected interference
  Not respond to BFRP (NDP Parsing failed)
    Resounding is time consuming
Cross-BSS UHR Sounding Procedure
AP-1
AP-2
STA-11
Associated with AP-1
UHR NDP Announcement
SIFS
SIFS
BFRP Trigger
SIFS
EHT Compressed Beamforming/CQI
EHT Sounding NDP
EHT Compressed Beamforming/CQI
STA-22
STA-11
STA-31
AP-1
AP-2
BSS-1
BSS-2
OBSS
NDP
NDP
STA-31
Associated with AP-1

## Slide 6: Proposal: Portion CSI Feedback between AP-to-AP
During cross-BSS sounding procedure, an AP that has initiated a multi-STA UHR sequential sounding may only convey the portion CSI feedback with high average SNR (in units of STA) to OBSS AP for computing Co-BF steering matrices without initiating resounding procedure in the following cases:
  When receiving the CSI feedback (with mixed average SNR) from all addressed STAs
    Eg, CSI with higher SNR from STA-11(Red arrow), CSI with lower SNR from STA-31(Black arrow)
  When receiving the CSI feedback (with higher average SNR) from part of addressed STAs
An OBSS AP that has received a portion CSI from an OBSS AP may compute the steering matrices by using the portion CSI during the Co-BF transmission procedure
AP-1
AP-2

## Slide 7
Summary
In this contribution, we proposed a operation to support that an AP can convey portion CSI feedback to OBSS AP for computing steering matrices during Co-BF procedure.

## Slide 8
Straw Poll 1
Do you support adding the following text to the SFD:
  An AP (either of the two APs) may convey the portion CSI feedback to the OBSS AP when performing Co-BF sequential NDP sounding procedure
    The AP that has received the portion CSI feedback shall compute Co-BF steering matrices based on the received portion CSI feedback

## Slide 9: References
[1] 802.11bn™/D0.2
[2] TGbn Motions List - Part 2