## Slide 1: Discussion on Time Synchronization in MAP Framework
Date: 2025-04-23
Authors:

## Slide 2: Abstract
Multi-AP (MAP) Framework has be defined in the 802.11bn™/D0.2[1]
Some MAP coordination (MAPC) operations require time synchronization, eg, Co-RTWT. However, the time synchronization mechanism still remains a open question in TGbn.
In this contribution, we discuss the time synchronization in the MAP framework

## Slide 3: Recap: Co-RTWT
[Motion #362, [2]]
A Co-RTWT Requesting AP shall include one or more Co-RTWT Parameter Set fields corresponding to each requested R-TWT schedule in the TBD individually addressed Management frame used for the request to the Co-RTWT Responding AP. The Co-RTWT Parameter Set field includes the following:
  Target Wake Time field
  Broadcast TWT ID field
  Broadcast TWT Persistence
  TWT Wake Interval Mantissa
  TWT Wake Interval Exponent
  Nominal Minimum TWT Wake Duration
  TBD other fields

## Slide 4: Observation
Co-RTWT operation
  The Responding AP as a TXOP holder shall ensure its TXOP ends before the start time of any active Co-RTWT SP for which protection is extended.
  The start time of a Co-RTWT is indicated by Target Wake Time field
Time synchronization is required for Co-RTWT operation
  Requesting AP may transmit the Co-RTWT Parameter Set with Target Wake Time field that is referenced to the TSF timer of the responding AP
Requesting AP
Co-RTWT SP
Extended Protection
Responding AP
TXOP ends
TXOP
Target Wake Time

## Slide 5: Proposal: Time Synchronization in MAPC Negotiation
Acquire Synchronization from MAPC agreement negotiation procedure
  After MAPC discovery procedure, the requesting AP shall transmit a MAPC Negotiation Request frame including Timestamp field that indicates the time info of AP-1 to the responding AP; and the responding AP shall respond with MAPC Negotiation Response frame including Timestamp field that indicate the time info of AP-2
Synchronization Maintaining
  The AP can maintaining Synchronization by recording the AP ID and the corresponding Timestamp field value
AP-1
(Requesting AP )
MAPC
Negotiation Req.
Timestamp -1
MAPC
Negotiation Resp. Timestamp -2
MAPC Discovery
AP-2
(Responding AP)
AP ID | Timestamp
AP-2 | Timestamp -2
… | …
AP ID | Timestamp
AP-1 | Timestamp -1
… | …
AP-1’s Table
AP-2’s Table

## Slide 6: Timestamp Field Design in MAPC Negotiation Request/Response Frame
Timestamp field in MAPC Negotiation Request/Response frame
  Timestamp field follows the AP ID subfield
 | Category | Public Action | Dialog Token | Negotiation MAPC Element
Octets: | 1 | 1 | 1 | variable
… | AP ID | Timestamp | …
MAPC Negotiation Request/Response frame format

## Slide 7: Summary
In this contribution, we discuss the time synchronization mechanism in the MAP framework. APs acquire time synchronization from the Timestamp field during the MAPC agreement negotiation procedure.
  Requesting AP includes Timestamp field in the MAPC Negotiation Request frame
  Responding AP includes Timestamp field in the MAPC Negotiation Response frame

## Slide 8: Straw Poll 1
Do you support adding the following text to the SFD:
  The requesting/responding AP may include Timestamp field in the MAPC Negotiation Request/Response Frame for time synchronization during MAPC agreement negotiation procedure

## Slide 9: References
[1] 802.11bn™/D0.2
[2] 24/0209r13 Specification Framework for TGbn