## Slide 1: Misc. CBF Topics part II
Date: 2025-05-14
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Srinath Puducheri | Broadcom |  |  | 
Karim Toussi | Broadcom |  |  | 
Dignus-Jan Moelker | Broadcom |  |  | 

## Slide 2: Introduction
Previously in 25/411 discussed two topics related to CBF sounding and CBF PPDU transmission
In this contribution discuss several more topics on the same subject

## Slide 3: Topic 1 – Sounding Reports Memory
Unlike SU BF or DL MU-MIMO, in COBF AP performs sounding based on other AP request (sequentially or jointly). We think that they need to advertise how many OBSS sounding reports they can store.
Propose two capability fields for the AP to store sounding reports as they consume memory on the device
  Capability 1 – N1: number of OBSS sounding reports that the AP can store at a time with N1<=4
  Capability 2 – N2: number of OBSS joint sounding reports that the AP can store at a time (N2<=N1)
Propose to limit N1 and N2 to 2 bits each:
  Do not expect more than 3-4 STA per AP participating in COBF at any given time.

## Slide 4: Topic 2 – COBF Sounding Feedback
Previously agreed on a mechanism for OBSS AP to signal max MCS it can hear in the feedback. Furthermore feedback for OBSS AP was also agreed to be limited to UL OFDMA
What about Nss? propose to limit Nss to 1 for OBSS AP sounding feedback for robustness and simplicity (can still use MCS choice for efficiency)
Furthermore since the majority of the market is comprised of 2x2 STA propose to limit the feedback rank (number of columns Nc) to 2

## Slide 5: Topic 3 – Sounding Feedback Padding
In COBF OBSS AP need to decode feedback of all STA in the other BSS.
Previously agreed that for COBF transmission T_PE is fixed as 20uS (nominal_packet_padding=20uS and aFactor=4)
 By a similar logic and to keep it simple propose to do the same for the sounding feedback

## Slide 6: SP#1
Do you agree to include the following into the 11bn SFD: APs exchange the following 2-bit capability fields with values 1,2,3 or 4 at the time of group formation between the members of a COBF pair. The capabilities are defined for the AP declared BW and assume Nc=2 (# of columns in the feedback)
  Field 1 – Total number of OBSS sounding reports that the AP can store for this COBF pair at a given time
  Field 2 – Total number of OBSS joint sounding reports that the AP can store for this COBF pair at a given time (can’t be higher than number in field 1)

## Slide 7: SP#2
Do you agree to include the following into the 11bn SFD: in the TB PPDU carrying OBSS AP sounding feedback do you support limiting Nss to 1?

## Slide 8: SP#3
Do you agree to include the following into the 11bn SFD : in COBF, cross-BSS/joint sounding feedback max Nc is limited to 2

## Slide 9: SP#4
Do you agree to include the following into the 11bn SFD : in TB PPDU carrying cross BSS (including joint) sounding feedback for COBF the T_PE is fixed as 20uS (nominal_packet_padding=20uS and aFactor=4) and LDPC extra symbol set as 1?
AP will set the UL length field and other parameters in the BFRP trigger frame according to this rule