## Slide 1: TXOP in P-EDCA
Date: 2025-04-30
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Zhenpeng Shi |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Below are two TXOP duration related paragraphs from IEEE802.11 REVme 7.0:
“The duration of a TXOP is the time a STA obtaining a TXOP (the TXOP holder) maintains uninterrupted control of the medium, and it includes the time required to transmit frames sent as an immediate response to TXOP holder transmissions. The TXOP holder shall, subject to the exceptions below, ensure that the duration of a TXOP does not exceed the TXOP limit, when nonzero.”
“In transmissions under EDCA by a STA that initiates a TXOP, there are two classes of duration settings: single protection and multiple protection. In single protection, the Duration/ID field of the frame can set a network allocation vector (NAV) value at receiving STAs that protects up to the end of any following Data, Management, or response frame plus any additional overhead frames as described below. In multiple protection, the Duration/ID field of the frame can set a NAV that protects up to the estimated end of a sequence of multiple frames.”

## Slide 3: Example of A TXOP
Below is an example of typical TXOP duration in multiple protection.
  Channel sensing and backoff before initiate a TXOP
  A TXOP is obtained through an initiate frame exchange (typically RTS/CTS)
  The TXOP holder indicate the expected TXOP duration through Duration field in each transmitted frame
  TXOP duration can be extended, but the total duration can not exceed the TXOP limit

## Slide 4: Some Ambiguities
In P-EDCA procedure, a DS-CTS frame is introduced before a short channel contention.
  The initial DS-CTS frame is used to suspend contention from non-P-EDCA eligible STAs
  The short channel contention is used for data transmission.
It is not clear whether the first part of P-EDCA contention period (DS-CTS and short backoff) is part of the TXOP?
If failure happens during P-EDCA contention period, when is the start time of the TXOP?

## Slide 5: Channel Protection in P-EDCA
The Duration field in DS-CTS protection the channel until the start of RTS frame (or a short time after the start of RTS);
The Duration field in RTS protection the channel until the end of the TXOP;
The third part STAs don’t have chance to attend the channel from the DS-CTS to the end of the TXOP;
The DS-CTS and the short contention should be a part of the TXOP.

## Slide 6: Option 1
The TXOP duration start from the DS-CTS that immediately precede the successful short contention that used for data transmission.
Case 1: without failure during P-EDCA contention period
Case 2: with failure during P-EDCA contention period

## Slide 7: Option 2
The TXOP duration start from the first DS-CTS frame to start P-EDCA contention in consecutive P-EDCA contention attempts that follows a successful short contention that used for data transmission.
Case 1: without failure during P-EDCA contention period
Case 2-1: with failure during P-EDCA contention period

## Slide 8: Option 2
More failure cases shows below
  If the channel is obtained by other STA in the middle of P-EDCA contention, then the TXOP starts from the DS-CTS of first consecutive P-EDCA attempts.
Case 2-2: with failure during P-EDCA contention period
Case 2-3: with failure during P-EDCA contention period

## Slide 9: Summary
P-EDCA is a new procedure introduced in TGbn;
Whether all or part of P-EDCA contention included in TXOP is not clear;
Two options for TXOP in P-EDCA procedure are proposed for discussion
Option 1 is slightly preferred due to simplicity.