## Slide 1: C-RTWT in NPCA Primary Channel
Date: 2025-04-30
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Zhenpeng Shi |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
A STA that supports non-primary channel access (NPCA) will switch to a non-primary channel when an OBSS PPDU is received;
C-RTWT responding AP and its association STAs will terminate TXOP before the start time of C-RTWT SP from a C-RTWT requesting AP;
NPCA and C-RTWT are two individual features for different purposes, but the spec need to clarify the C-RTWT operation when C-RTWT responding AP and its association STAs switch to NPCA primary channel.

## Slide 3: General Rules
Generally, after Co-RTWT Responding AP and its associated STAs switch to NPCA primary channel, they should terminate the obtained TXOP before the start time of Co-RTWT SPs;
  The TXOP holder on primary channel may terminate TXOP before the start time of Co-RTWT SP according to R-TWT or Co-RTWT rules
  The contention of Co-RTWT requesting AP after the start time of Co-RTWT SP may occupy the whole operating bandwidth, it will conflict with the transmission on NPCA primary channel.
Co-RTWT Responding AP & its associated STA
Co-RTWT Requesting AP
Associated STA of Requesting AP
RTS
CTS
PPDU1
BA
CF-
END
Original TXOP
Start time of Co-RTWT SP
Primary Channel
NPCA Primary Channel
PPDU2
Collision?

## Slide 4: Exception Rule 1
If Co-RTWT Responding AP switch to NPCA primary channel base on a long PPDU from Co-RTWT requesting AP’s BSS, then Co-RTWT Responding AP doesn’t need to terminate obtained TXOP on NPCA primary channel before the start time of Co-RTWT SP;
  The requesting AP is transmitting or receiving on primary channel, no new contention will start before the end of the long PPDU
  The NPCA primary channel will totally not overlapped with the transmitting channel of the long PPDU
  No interference between NPCA transmission and long PPDU on primary channel
Co-RTWT Responding AP & its associated STA
Co-RTWT Requesting AP
Associated STA of Requesting AP
RTS
CTS
PPDU
BA
Start time of Co-RTWT SP
Primary Channel
Primary Channel
NPCA Primary Channel

## Slide 5: Exception Rule 2-1
If Co-RTWT Requesting AP’s operating channel doesn’t overlap with Co-RTWT Responding AP’s NPCA channel, Co-RTWT Responding AP doesn’t need to terminate TXOP on NPCA primary channel before the start time of Co-RTWT SP;
The Co-RTWT Responding AP can also informs its associated STAs not to terminate TXOP on NPCA primary channel before the start time of Co-RTWT SP under this case.
Below is an example of 160MHz and 320MHz for Co-RTWT Requesting AP’s and Co-RTWT Responding AP’s operating channel respectively. Same rule applies for 80MHz and 160MHz for Co-RTWT Requesting AP’s and Co-RTWT Responding AP’s primary channel respectively.
160 MHz
160 MHz
Co-RTWT Requesting AP’s operating channel
Co-RTWT Responding AP’s operating channel
Co-RTWT Responding AP’s NPCA Channel

## Slide 6: Exception Rule 2-2
Below is another use case for exception rule 2.
  Co-RTWT requesting AP and Co-RTWT responding AP have common primary 160MHz;
  Co-RTWT requesting AP and Co-RTWT responding AP have different secondary 160MHz due to 320MHz -1 and 320 MHz-2 channelization
  Co-RTWT responding AP’s selects the secondary 160MHz as NPCA primary channel
  As a result, Co-RTWT responding AP’s NPCA primary channel (consider no preamble puncture) will not overlap with Co-RTWT requesting AP’s operating channel.
160 MHz
160 MHz
320MHz -2
320MHz -1
Co-RTWT Responding AP’s secondary 160 MHz
160 MHz
Common primary 160 MHz
Co-RTWT Responding AP’s secondary 160MHz

## Slide 7: Summary
The operating rules of Co-RTWT in NPCA primary channel are discussed;
Generally, the responding AP and its associated STA should protect the start time of Co-RTWT SP;
In some cases, if responding AP’s NPCA channel not overlap with the communicating channel of requesting AP, the responding AP doesn’t need to terminate TXOP before the start time of requesting AP’s Co-RTWT SP.