## Slide 1: Remaining Issues of AMP PPDU Design
Date: 2025-05-12
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Ke Wang |  |  |  | 
Shengjiang Cui |  |  |  | 
Zhisong Zuo |  |  |  | 
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 2: Abstract
In this contribution, we discuss the remaining open issues in AMP PPDU design covering issues such as non-AMP preamble configuration, synchronization, SIG and data fields, DL/UL waveform generation, PPDU format and UL transmission configuration.
Doc.: IEEE 802.11-25/0790r0

## Slide 3
Non-AMP DL Preamble Format
  Non-AMP legacy preamble includes L-STF, L-LTF, L-SIG, RL-SIG, and U-SIGs for Active Tx and AMP enabled devices
  For backscattering AMP device, additional preamble format, e.g., 802.11b like preamble can be used
    Single carrier DSSS
    Depending on the waveform of the following AMP portion
  Convergence is possible when AMP portion waveform is decided.
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 4
Non-AMP DL Preamble Configuration
  Configuration of L-SIG
    Rate: configured as an unsupported rate
      Differentiate from WUR where rate is always configured as MCS0
      Other legacy devices can stop reception once detecting unsupported rate
    Length: configured as entire DL PPDU including excitation field(s)
      UL transmission parameters, e.g., payload size, rate, MCS, etc., are all configured by the AMP AP
  Configuration of RL-SIG
    Instead of repetition of L-SIG, may consider other options, e.g., complement of L-SIG, to differentiate 802.11bp PPDU from legacy PPDU
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 5
Non-AMP DL Preamble Configuration
  Configuration of individual fields in U-SIG
    Two U-SIG formats available but need to choose only one for 802.11bp
      EHT MU PPDU can be chosen
    How to differentiate 802.11bp PPDU from 802.11be and 802.11bn PPDU?
      Validation fields, e.g., version
      For example, version field can be configured different from 802.11be and 802.11bn
    UL/DL: configured as DL if there is no excitation field and UL otherwise
    Txop can be configured as maximum value, so it actually does not indicate Txop duration.
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 6
AMP Synchronization
  Asymmetric synchronization design for UL and DL
    Different sync sequences in terms of pattern and/or length for DL/UL to differentiate UL and DL
  DL synchronization design
    In our companion contribution [1], it is shown that DL synchronization performance depends on sequence length, chip duration, sampling rate, etc.
      Sequence length: 16 and/or 32
      Sampling rate: 2MHz or 8MHz
      Chip duration: same chip duration for 1Mbps and 250kbps for reduced complexity at AMP non-AP STA side: 0.5, 1 and 2 microsecond can be considered
    Main findings: cross-correlation with data portion may cause severe sync inaccuracy
  UL synchronization design
    A single synchronization sequence can be used for multiple data rates
    Chip rate can scale with data rate and short chip duration is used for higher rate with higher SNR to reduce signalling overhead
    AP does not need to do blind detection trying various chip duration with knowledge of UL transmission configuration.
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 7
SIG Field and Payload Size
  DL SIG fields: length and/or payload size, backscatter indication, UL configuration to configure the following UL transmission in followed excitation field, CRC
  Alternatively, these information can also be conveyed in MAC header
  If in SIG, these basic information can always be transmitted with low rate for better link budget.
  Flexible payload size configuration for DL and UL
    Multiple frame formats need to be supported in DL including data, management and control frames
    For data frame, 802.11ba can still be a starting point
      Frame body is m*n
        m is the size of AMP non-AP STA ID, e.g., AID or compressed AID
        n is the number of AMP non-AP STAs to be addressed
    For UL, some fixed payload size can be defined to reduce signalling overhead and padding can be applied if needed.
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 8
DL/UL waveform generation
  Agreement: The carrier waveform for AMP Downlink PPDU is constructed by repeating one predefined base waveform of TBD micro-second, we suggest having a bandwidth of 10M.
  DSSS
    Replace Barker code with another spreading code, which can generate a narrow bandwidth DSSS signal
    BW flexibly depends on the spreading code
  OFDM
    OFDM BPSK sequence to generate a narrow bandwidth OFDM signal as the predefined base waveform for around 10MHz.
    BW 10MHz leave sufficient guard band for various implementations [2].
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 9
DL PPDU: Flexible BW and Waveform
  DL PPDU
    Different BW and waveforms can be considered for different fields including preamble, excitation, data, etc., to achieve optimized performance.
  Active Tx
    Preamble: 20MHz with OFDM waveform
    AMP part: no less than 10 MHz but can be DSSS waveform
  Backscattering
    Preamble: OFDM or DSSS
    AMP part
      All transmitted by the same node for mono-static case  unified design
      Different fields can be transmitted by separated nodes for bi-static case  different design for data portion and excitation
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 10
PPDU Format
  New DL PPDU format
    Legacy nodes, e.g., existing legacy APs, mobile phones, as energizers could be without AMP protocol support
    AMP AP configures energizer and AMP non-AP STA with DL PPDU
    Energizer then transmits excitation to be used for AMP non-AP STA backscattering. Due to co-existence requirement, a legacy non-AMP preamble needs to be transmitted before the excitation field. Thus, a new PPDU format is needed.
  Decouple DL and UL for backscattering AMP non-AP STAs
Doc.: IEEE 802.11-25/0790r0
May 2025
Notes: Preamble + Sync + excitation

## Slide 11
UL Configuration
  Chip duration can scale with data rate and FEC coding
    For example, 2us for 250kbps without FEC coding and 1us with FEC coding.
  UL BW, e.g., BW of the main lobe, can also scale with data rate.
    Narrower BW for lower data rates.
  UL BW can also scale with data rate.
    FDM may be applied at least for low data rate
Yinan Qi (OPPO)
Slide 11
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 12
UL Configuration: MCS
  FEC coding, e.g., convolutional coding with coding rate 1/2, can be supported for UL with 2.5dB coding gain [3]
  A baseline MCS table can be as follows.
    Rate has been decided with or without FEC coding
    Chip duration will change with FEC coding rate.
Yinan Qi (OPPO)
Slide 12
Doc.: IEEE 802.11-25/0790r0
May 2025
MCS Index | Device Type | FEC Coding Rate | Data Rate
0 | Backscattering AMP device and Active AMP device | 1/2 | 250 kbps
1 | Backscattering AMP device and Active AMP device | 1 | 250 kbps
2 | Backscattering AMP device and Active AMP device | ½ | 1 Mbps
3 | Backscattering AMP device and Active AMP device | 1 | 1 Mbps
4 | Active AMP device | ½ | 4 Mbps
5 | Active AMP device | 1 | 4 Mbps

## Slide 13
Summary
  The following issues are discussed and analysed in this contribution
    Preamble design
    Synchronization design for both DL and UL
    DL/UL SIG and payload size
    DL/UL waveform generation
    DL PPDU format
    UL configuration, e.g., MCS
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 14: Reference
[1] “Sync field for AMP PPDU,” IEEE 802.11-25/0801r0, May 2025
[2] “OOK generation for AMP,” IEEE 802.11-25/0802r0, May 2025
[3] “AMP UL Transmission,” IEEE 802.11-25/0317r0, Mar. 2025
Doc.: IEEE 802.11-25/0790r0
May 2025

## Slide 15: SP 1
Doc.: IEEE 802.11-25/0790r0
May 2025
  The preamble of an AMP DL PPDU for AMP enabled non-AP STA and active TX non-AP AMP STA should be configured as follow,
    L-SIG
      Rate - configured as an unsupported MCS level
    U-SIG
      Version field - configured different from 802.11be and 802.11bn
      UL/DL - configured as DL if there is no excitation field and UL otherwise
  Other fields are TBD

## Slide 16: SP 2
Doc.: IEEE 802.11-25/0790r0
May 2025
  IEEE 802.11bp will specify, in 2.4 GHz, DL synchronization sequence with the same chip duration for all data rates for non-backscatter case.

## Slide 17: SP 3
Doc.: IEEE 802.11-25/0790r0
May 2025
  IEEE 802.11bp will specify, in 2.4 GHz, a single UL synchronization sequence for all data rates for non-backscatter case.

## Slide 18: SP 4
Doc.: IEEE 802.11-25/0790r0
May 2025
  IEEE 802.11bp will specify additionally, in 2.4 GHz, an AMP PPDU format containing an 802.11 preamble field and an excitation field for bi-static use case. This PPDU is transmitted by the energizer to the backscatter non-AP AMP STA.

## Slide 19: SP 5
Doc.: IEEE 802.11-25/0790r0
May 2025
  For DL PPDU and UL PPDU for non backscattering case:
  For AMP Manchester encoded OOK of rate 250kbps, each data bit is encoded based on the chip duration of 2us.
  For AMP Manchester encoded OOK of rate 1Mbps, each data bit is encoded based on the chip duration of 0.5us.
  For AMP Manchester encoded OOK of rate 4Mbps, each data bit is encoded based on the chip duration of 0.125us.

## Slide 20: SP 6
Doc.: IEEE 802.11-25/0790r0
May 2025
  IEEE 802.11bp will specify, in 2.4 GHz, convolutional coding with coding rate ½ for UL transmission. The details of encoder is TBD.