## Slide 1: Follow up on Correspondence between Energizers and AMP non-AP STAs
Date: 2025-05-12
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Doc.: IEEE 802.11-25/0792r0
May 2025

## Slide 2: Abstract
In this contribution, we discuss further details for the correspondence between energizer and AMP non-AP STAs needed for WPT and excitation signals.
Doc.: IEEE 802.11-25/0792r0

## Slide 3
Recap of Correspondence
  A correspondence table can be established between energizers and AMP non-AP STAs.
  How to establish such correspondence table?
    Energizer initiated
    AP initiated
    Sounding between energizer and AMP devices + CSI feedback
    Position reporting from energizer and AMP devices
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0792r0
May 2025
 | Energizer A | Energizer B
AMP a | √ | X
AMP b | X | √

## Slide 4
Consequences without Correspondence
  Multiple energizers are activated to transmit excitation/WPT signals for a target AMP non-AP STAs
    Low efficiency
    AMP non-AP STA may not be able to process multiple excitation signal
  Even with only one energizer activated, without good correspondence higher interference may happen
    Energizer B is activated instead of energizer A
    Direct link between AMP AP and energizer B cause heavy interference.
  A far away energizer may be activated thus energy harvesting is with low efficiency or even not successful.
    Energizer B is activated even it is far away from target AMP non-AP STA
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0792r0
May 2025

## Slide 5
How to Establish the Correspondence Table?
  Position reporting based method
    Limited by complexity and power consumption
      High accuracy positioning method normally requires Tx/Rx positioning signals and high processing capability
      AMP AP and energizer can be located with relatively good accuracy
      AMP non-AP STA may not due to low complexity not supporting high accuracy positioning method
    Highly depend on positioning accuracy
      In [1], it shows that the range for bi-static backscattering AMP devices can be only a couple of meters without enhancement.
      Considering 1m positioning accuracy, error can be up to 50% of total range.
    Without good positioning accuracy, a wrong energizer might be activated and it may not be able to sufficiently charge the target AMP devices.
  Channel measurement based method
    Essentially distance/position based method
    Limited by measurement capability of AMP devices.
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0792r0
May 2025

## Slide 6
Energizer ID based Method
  Exchange of energizer ID is more feasible
    Energize sends WPT/excitation signal together with the energizer ID when instructed by the AMP AP
    AMP non-AP STA then reports such ID
  Two issues:
    How does the AP instruct the energizer?
    How does the energizer transmit is own ID.
  Solution to these issues can be different for WPT signal and excitation signal.
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0792r0
May 2025

## Slide 7
How to Signal the ID?
  WPT signal
    AP includes an indication bit in the control information sent from AP to the energizer.
    Energizer can send its ID in 2.4GHz separately from WPT signal in S1GHz.
      Energizer should establish a link between its ID and particular WPT signal
    Energizer can send its ID in S1GHz together with WPT signal
      WPT PPDU
      AMP PPDU if S1GHz communication is specified.
  Excitation signal
    When energizer transmits excitation signals, it is always in 2.4GHz.
    AMP AP can transmit energizer’s ID in the AMP DL PPDU to the target AMP non-AP STA, e.g., MAC header.
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0792r0
May 2025

## Slide 8
Without Correspondence
  Correspondence availability
    Correspondence is not available at the very beginning before transmission of any WPT/excitation/communication signal.
    Once correspondence is established gradually with WPT/excitation/communication signal transmission, such correspondence table can be used to optimize the following WPT/excitation signal.
  Without correspondence
    AP broadcasts to activate all energizer.
      Interference for excitation signals
      For WPT signal, it will block channel as long as there is energizer deployed
      AMP non-AP STA cannot decode ID of energizers
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0792r0
May 2025

## Slide 9
Without Correspondence
  AMP AP can activate the energizer group by group or one by one until the target AMP non-AP STA is activated or charged.
  For example, AMP AP sets periodic time slot 1-4, within which energizer or energizer group can be activated to transmit WPT/excitation signals.
  Each energizer or energizer group can then choose one of the slots to transmit its own signal based on AP configuration.
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0792r0
May 2025
Slot 1
Slot 2
Slot 3
Slot 4
t
Energizer 1/group 1
Energizer 1/group 2
Energizer 1/group 3
Energizer 1/group 4

## Slide 10
Summary
  In this contribution, we discussed further details on how to establish correspondence table between energizers and AMP non-AP STAs.
Yinan Qi (OPPO)
Slide 10
Doc.: IEEE 802.11-25/0792r0
May 2025

## Slide 11: Reference
[1] “UL Monostatic and Bistatic Range Extension Considerations,” IEEE 802.11-25/0307r0, Mar. 2025
Doc.: IEEE 802.11-25/0792r0
May 2025

## Slide 12
SP1
  Do you agree to capture the following text to TGbp SFD?
    The correspondence between energizer and AMP devices that determines which energizer to activate to charge target AMP devices should be supported
Yinan Qi (OPPO)
Slide 12
Doc.: IEEE 802.11-25/0792r0
May 2025