## Slide 1: AMP Carrier Waveform: follow-up Downlink and Backscattering
Date: 2025-05-12
Authors:

## Slide 2: Introduction
Carrier waveform is used for DL OOK modulation, UL backscattering modulation, tag excitation/energizer
The performance of carrier waveform for backscattering PPDU is investigated [2]
  OFDM ~= DSSS
  L-LTF was analyzed as the OFDM carrier waveform
March meeting motion:
  Carrier waveform is defined based on repeated base waveform with phase randomization
Two further questions:
  How to standardize base waveform?
  How to design OFDM carrier waveform?

## Slide 3: Carrier Waveform
Prefer OFDM symbol as base waveform
  Compatible with 802.11 OFDM preamble, already agreed in 11bp
  Reuse existing OFDM symbol definition, e.g. LTF, STF, etc.
    Easier reader implementation, no need to go through data path
    Avoid endless waveform optimization debates in WUR
      Challenging and do not expect much gain, considering tag ppm and random timing
Prefer to standardize the carrier waveform in 11bp
  Tag design can optimize the envelope detector based on waveform
  Reader to optimize leakage cancellation, especially in bi-static case
    Easy interop, for certification definition
  Avoid the uncertainty and complexity for WUR waveform
Payload
Payload
Tag
Excitation
Excitation
OFDM Preamble
SYNC
UL SYNC
Reader

## Slide 4: OFDM Carrier Symbol Selection Criteria
Tx power:
  Spectrum close to random data  low PAPR
OOK “ON” waveform power variation
  DL modulated portion (SYNC, payload) and backscattering UL PPDU
  “ON” symbol power = Manchester bit detection SNR
    Manchester bits without FEC coding
  Random timing and high ppm at tag
    DL Rx detection and UL Tx OOK modulation
  Two rates: 2us “ON” (250kbps), 0.5us “ON” (1Mbps)
Payload
Payload
Tag
Excitation
Excitation
OFDM Preamble
SYNC
UL SYNC
Reader

## Slide 5: “ON” Power Variation
 | …
DL OOK:
  Reader can modulate on OFDM symbol boundary
  Tag Rx samples the waveform at random timing (2/4/8MHz) and ppm
UL backscattering OOK:
  Tag modulates with random timing and ppm on OFDM waveform
  xdB variation will cause xdB reader performance loss
  Two rates: 250Kbps2us “ON” and 1Mbps  0.5us “ON”
 | …
2us | 2us
2us | 2us
Carrier Symbol
0.5 us | 0.5 us | 0.5 us | 0.5 us | 0.5 us | 0.5 us | 0.5 us | 0.5 us
 | …
2us | 2us
2us | 2us
0.5 us | 0.5 us | 0.5 us | 0.5 us | 0.5 us | 0.5 us | 0.5 us | 0.5 us
DL
UL
UL

## Slide 6: OFDM Carrier Symbol Candidates
Carrier Symbol
  Bandwidth: 20MHz with existing tone plan
    Low-cost tag practically has no analogue filter, ~80MHz responsive.
    Higher Tx power
  Duration: 4us  smaller OOK power variation
Existing symbols with Low PAPR
  STF symbol: L-STF (0.8us), HE TB STF (1.6us)
    False trigger to WiFi devices or uncertain packet detection state machine.
  LTF symbol: L-LTF, VHT-LTF, HE-1xLTF
    Simple implementation. Preferred option.
New symbol with QAM sequence
  Large search space with limited benefits

## Slide 7: AMP Reader Tx Architecture
IFFT
Up-sampling and Tx filter
DAC
PA
OOK Modulation
Tx filter will be able to suppress some spectrum growth due to OOK modulation
PA distortion is symbol-content dependent

## Slide 8: “ON” Power: 250kbps (2us chip)
All sequence has similar range: ~0.5dB
Symbol | Power swing (dB)
HE_STF TB | 0.2
HE_LTF_1x | 0.6
LLTF | 0.6
VHT_LTF | 0.4
New Sequence [1] | 0.5

## Slide 9: “ON” Power: 1Mbps (0.5us chip)
All sequence has similar range: ~2dB
VHT_LTF is 0.5dB better
Symbol | Power swing (dB)
HE_STF TB | 1.1
HE_LTF_1x | 2.6
LLTF | 2.1
VHT_LTF | 1.6
New Sequence [1] | 2.2

## Slide 10: Spectrum: Low Power
RBW: 100kHz

## Slide 11: VHT-LTF, OOK, Low power
RBW: 100kHz

## Slide 12: L-LTF, OOK, Low power
RBW: 100kHz

## Slide 13: Spectrum: High Power
RBW: 100kHz

## Slide 14: DL Spectrum: L-LTF, OOK, High power
RBW: 100kHz

## Slide 15: DL Spectrum: VHT-LTF, OOK, High power
RBW: 100kHz

## Slide 16: Summary
The carrier base waveform needs to have good properties
  Support high Tx power
  Limited spectrum growth with OOK modulation
  Low OOK power variation: random offset and ppm
  Easy WiFi reader implementation
Suggest to standardize the carrier base waveform using existing 20MHz 4us OFDM symbol
  L-LTF or VHT-LTF

## Slide 17: SP
Do you agree to add the following to 11bp SFD?
The SYNC, Data field and Excitation field of 11bp DL PPDU use OFDM symbol as base carrier waveform for OOK modulated communication.

## Slide 18: SP
Do you agree to add the following to 11bp SFD?
The base OFDM symbol is defined as 4us OFDM symbol, and generated by performing 64-point IFFT of the predefined sequence and pre-append the last 0.8us waveform as the cyclic prefix

## Slide 19: SP
Do you agree to add the following to 11bp SFD?
The frequency domain sequence for the base OFDM symbol is the same as the one defined for L-LTF

## Slide 20: Reference
[1] 11-25/0325, Steve, amp-downlink-bandwidth-control-using-ofdm-spreading-waveform.pptx
[2] 11-25-0305-00-00bp-AMP-Downlink-and-Backscattering-Carrier-Waveform

## Slide 21: Appendix

## Slide 22: Carrier Waveform Considerations
Format uniformity for DL PPDU
  OFDM preamble  OFDM carrier waveform
  DSSS preamble  DSSS carrier waveform
  Mixed format is not preferred unless necessary: Easy to implement at WiFi Reader
Repeated carrier waveform is preferred for OOK modulation in backscattering operation
  Easier for Tx implementation
  Automatically serve as reference symbol for leakage estimation
AMP Data | … | AMP Data | Reference Symbol | Reference Symbol | Excitation Symbol | … | Excitation symbol

## Slide 23: Carrier Waveform Considerations
Low PAPR waveform candidates
Single-tone CW:
  Tx power limitation in some regions  >10MHz BW was agreed
DSSS waveform
  Single carrier waveform, 2~3dB
OFDM waveform
  STF symbol (~2dB): may cause legacy WiFi devices to false detect
  LTF symbol (~3dB): preferred
  Newly optimized symbol: flexible BW, non-BPSK signal
    Added complexity with limited benefits

## Slide 24: L-LTF OOK
2us
2us | 2us
2us | 2us
0.5 us | 0.5us
0.5 us | 0.5us
0.5 us | 0.5us
0.5 us | 0.5us
0.5 us | 0.5us
0.5 us | 0.5us
0.5 us | 0.5us
0.5 us | 0.5us
0.5 us | 0.5us
0.5 us | 0.5us

## Slide 25: High Power

## Slide 26: Low Power

## Slide 27
 | Tx Power Gain over New Sequence [1]
VHT-LTF, 1Mbps | 0.77
VHT-LTF, 250kbps | 0.69
L-LTF, 1Mbps | 0.32
L-LTF, 250kbps | 0.49