## Slide 1: AMP OOK Simulation Methodology and Baseline Results
Date: 2025-05-12
Authors:

## Slide 2: Introduction
On-OFF keying (OOK) has been agreed as the modulation scheme for AMP
As the group progresses to finalize the PHY design, it is important to align on the simulation methodology
  Calibrate the results among different contributions
  Compare the performance of various designs
Main impairments to model for OOK performance
  Tag clock ppm
  Tag/Reader AGC behavior

## Slide 3: DL OOK Sim Diagram
2: AWGN + AGC model
  Normalize noise to –x dB
  Scale OOK signal accordingly to SNR
  ADC quantization
  Ideal setting:
      X = 0dB, ADC quantization omitted
  Practical setting:
      X = -6dB (SNR ceiling)
      3~4 bit ADC quantization
1: base waveform of duration W (us)
  Pulse, OFDM, and random polarity added
3: Tag clock ppm resampling:
  Random first sample delay: [0, 80*W]
  Resample the Rx signal at 80MHz * (1+ppm)
4: Envelope detector and down-sample:
  ED output = sum(|y|) / (1+ppm),
    sum over 80MHz/clock_rate samples
    ED output at clock rate, 2MHz/4MHz/etc.
1
Base waveform
OOK Modulation
Envelope detector down-sample
channel
ppm resampling
SYNC/Data detection
AWGN+ AGC
80MHz
80MHz
80MHz
2
3
4
0 1 1 0 0 …
Reader
Tag
2/4/8MHz

## Slide 4: UL OOK Sim Diagram
Base waveform
OOK Modulation
1: Base waveform of duration W (us)
  Pulse, OFDM, and random polarity added
2: Tag ppm resampling
  Random first sample delay: [0:0.25:20*W]
  Resample the signal at 20MHz * (1+ppm)
channel
ppm resampling
SYNC/Data detection
AWGN+ AGC
20MHz
20MHz
Tag clock
3: AWGN + AGC model
  Normalize noise to –x dB
  Scale OOK signal accordingly to SNR
  ADC quantization
  Ideal setting:
      X = 0dB, ADC quantization omitted
      Works for active Tx UL
  Practical setting for BS:
      X = -12dB or other number
      10-bit ADC quantization
  4: Data detection:
    Coherent or Non-coherent
1
2
3
ADC
4
Reader
Tag
0 1 1 0 0 …

## Slide 5: Simulation Settings
Simulation diagram:
  Slide 3 and 4
Carrier waveform:
  Pulse: square pulse
  OFDM: L-LTF
Detectors
  Coherent and non-coherent
  Ideal timing and per-bit re-timing
Ideal AGC
Clock accuracy: 0 ppm
Payload: 100 bits

## Slide 6: DL OOK Baseline Results: 250kbps

## Slide 7: DL OOK Baseline Results: 1Mbps

## Slide 8: DL Sim Baseline Results: Summary
Performance of OFDM carrier waveform is similar to pulse carrier
Per-bit timing has ~0.7dB loss from ideal timing
Sensitivity | 250kbps, non-Coherent |  | 1Mbps, non-Coherent | 
 | Ideal Timing | Non-Ideal Timing | Ideal Timing | Non-Ideal Timing
Pulse | -7 | -6.3 | -3.3 | -2.6
OFDM | -6.9 | -6.2 | -3.0 | -2.2

## Slide 9: BS Sim Baseline Results: 250kbps

## Slide 10: BS Sim Baseline Results: 1Mbps

## Slide 11: BS Sim Baseline Results: Summary
Sensitivity | 250kbps, Coherent |  | 1Mbps, Coherent | 
 | Ideal Timing | Non-Ideal Timing | Ideal Timing | Non-Ideal Timing
Pulse | -9.3 | -7.4 | -3.3 | -1.2
OFDM | -9 | -7.3 | -2.9 | -0.6
Sensitivity | 250kbps, non-Coherent |  | 1Mbps, non-Coherent | 
 | Ideal Timing | Non-Ideal Timing | Ideal Timing | Non-Ideal Timing
Pulse | -3.5 | -2.6 | 0.3 | 1.4
OFDM | -3.4 | -2.4 | 0.7 | 2.1
Performance of OFDM carrier waveform is similar to pulse carrier (<1dB)
Per-bit timing has 1~2dB loss from ideal timing
Coherent detector has ~5dB gain for 250kbps and ~3dB gain for 1mbps

## Slide 12: Discussions
Carrier waveform for simulation
  Square pulse waveform is slightly better than 20MHz OFDM
  The detector type has big impact to the performance
Simulation setting suggestions:
  Rx waveform: x us noise before actual PPDU
    Test SYNC false trigger rate from noise
    Backscattering tag: 400us noise before actual PPDU
      +/-10% of ~2ms tag processing time
    Non-backscattering tag: 5ms
  Tag clock ppm:
    Backscattering Tag with OOK modulation: 100kppm
    Active Tag: 1000ppm for Tx, 10kppm Rx?
    AMP enabled WiFi: 1000ppm for Rx?

## Slide 13: SP
Do you agree to simulate OOK performance using the diagram as show in slide 3 and 4?
Note: opinion collection

## Slide 14: SP
Do you agree to add the following 11bp SFD?
The maximum allowed clock inaccuracy for the backscattering tag using OOK modulation is 100,000 ppm for both receive mode and backscattering transmit mode?