## Slide 1: Follow up on Duty-cycle operation for AMP
Date: 2025-05-02
Authors:
Doc.: IEEE 802.11-25/0813r0
May 2025
Name | Affiliation | Address | Phone | Email
Chuanfeng He | OPPO |  |  | hechuanfeng@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Yinan Qi |  |  |  | v-qiyinan@oppo.com

## Slide 2
Background
  For AMP communication, power storage is necessary for AMP STA to supply the operation power when simultaneously harvested power only is not enough to cover the consumed power[1].
  Power saving from duty cycle
    It is challenging for AMP STA to perform consistent monitoring for potential AMP trigger for uplink transmission due to limited power storage.
    Duty-cycle operation can reduce the time duration of AMP STAs Rx, which are the main contributors of power consumption during awake time.
  The motions related to duty cycle operation were agreed [2].
  MM-1: If AMP device is able to support AMP TSF, the maximum timing offset is ±104 ppm.
  MM-2: 11bp defines a mechanism to allow an AP to solicit AMP uplink PPDU(s) from one or more 802.11bp clients.
  MM-4: If an AMP device is able to support TSF, it can monitor AMP DL Frame in a duty-cycle manner.
Chuanfeng He (OPPO)
Slide 2
Doc.: IEEE 802.11-25/0813r0
May 2025

## Slide 3
Duty cycle operation for use cases
  Logistics like use cases: short term detection and identification
    Short latency is required for quick trigger detection and uplink transmission for AMP STA identification.
    Small form factor is required. Capacitor is used for energy storage from RF power harvesting.
    Short duty cycle is assumed to address low latency and limited awake duration. Typical duty cycle may be several or dozens of milliseconds.
  Sensor like use cases: long term monitoring and reporting
    The reporting frequency of sensor data is low. Short awake duration for reporting and long idle duration for power save can be assumed.
    Capacitor or solid-state battery can be equipped for energy storage. Ambient power other than RF can be supported, e.g. solar.
    Long duty cycle can be used to allow power save. Typical duty cycle may be several minutes or hours.
Chuanfeng He (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0813r0
May 2025

## Slide 4
Duty-cycle configuration at AP side
  Operation at AP side[3]
    AP sends AMP trigger frames following trigger interval[4]
      To facilitate initial trigger detection during initial trigger searching window of AMP STAs.
    Information carried in AMP trigger frame[4]
      Timestamp to align the local TSF timer of AMP STAs
      Duty-cycle configuration
        Duty cycle parameters, e.g. Trigger interval, service period length
        Information for AMP STA to determine specific duty cycle period and service periods
Chuanfeng He (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0813r0
May 2025

## Slide 5
Duty-cycle operation at AMP STA side
  Operation at AMP STA side[3]
    AMP STA monitors AMP trigger during initial trigger searching window to obtain
      Timestamp
      Duty-cycle configuration
    AMP STA derives its specific duty cycle period and service periods
      AMP STA or STA group specific Duty-cycle operation, with specific service periods
        Reduce power consumption through less trigger monitoring
        Spread AMP STAs to trigger sets to reduce collision
        AMP STA grouping randomly or based on predefined rules
    AMP STA matches its service periods to the target AMP trigger transmission time windows, based on its Duty-cycle configuration and local TSF timer.
Chuanfeng He (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0813r0
May 2025

## Slide 6
Duty-cycle operation at AMP STA side
  Specific Duty-cycle operation, for example
    Trigger interval: 20ms
    Duty cycle period: 200ms
    Duration of service period: 7ms
    Specific service periods for AMP STA 0-9
      Specific time offset for each AMP STA
Chuanfeng He (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0813r0
May 2025

## Slide 7
Energy storage and power consumption model
  The following analysis focuses on logistics like use cases.
    AMP STA
      A capacitor of 12µF [4]
      Operating Voltage: 1.5V
      Discharge Cut-off Voltage: 1.25V
      Operating Current: 10µA
    Available energy with fully charged capacitor
      Total energy: 12µF*1.5^2/2=13.5µJ
      Residual energy: 12µF*1.25^2/2=9.375µJ
      Available maximum energy storage for operating: 4.125µJ
    Power consumption model
      Sync detection: 15µW with 1.5V and 10µA
      Trigger frame Rx and decoding: 100µW[5]
      Solicited data Tx: 200µW
      Idle power :0.1µW
Chuanfeng He (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0813r0
May 2025

## Slide 8
Operating during initial trigger searching window(ITSW)
  Initial trigger searching window(ITSW)
    The window of continuous initial trigger searching, after AMP STA initially wakes up upon enough energy storage.
    AMP STA acquires TSF and duty cycle configuration through initial trigger.
    Duration of ITSW: 20ms, assuming trigger interval is 20ms.
  Energy consumption during ITSW
    Energy consumption for sync detection: 15µW*20ms=0.3µJ.
    Energy consumption for initial trigger frame Rx: 100µW*0.5ms=0.05µJ, trigger PPDU length=500µs
    Total energy consumption: 0.3+0.05=0.35µJ
Chuanfeng He (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0813r0
May 2025

## Slide 9
Operating during Duty-cycle operation
  Normal service period (NSP)
    Once AMP STA detects a AMP trigger during ITSW, it can monitor further AMP trigger in a duty-cycle manner through normal service period.
    Duty cycle period =200ms.
    Duration of NSP: 7ms
      2ms early wake-up in each duty cycle period (to address 10^4 ppm clock drift).
      Time Window for AP to send trigger is 5ms.
    Trigger PPDU length=500µs. Solicited UL PPDU length= 500µs.
  Energy consumption during duty cycle with periodical NSP
    0.1µW idle power is neglectable.
    Energy harvesting between NSPs is ignored.
    During the duty-cycled operation procedure(e.g., every 7ms NSP within 200ms duty cycle period), we assume that at most 10 NSPs are needed in order to detect the target trigger soliciting UL data for the AMP STA.
Chuanfeng He (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0813r0
May 2025

## Slide 10
Operating during Duty-cycle operation
    Energy consumption
      In each duty cycle, energy for sync searching: [2ms + 5ms =7ms] * 15µW=0.105µJ;
      Energy consumption for total 10 NSPs for sync searching: 10*[2ms + 5ms =7ms] * 15µW=1.05µJ;
      Energy consumption for total 10 NSPs for trigger frame Rx: 10*100µW*0.5ms=0.5µJ
      Energy consumption for solicited data Tx: 200µW*0.5ms=0.1µJ.
      Total energy consumption: 1.05+0.5+0.1=1.65µJ
Chuanfeng He (OPPO)
Slide 10
Doc.: IEEE 802.11-25/0813r0
May 2025
Total energy consumption between wake-up and end of solicited UL data Tx: 0.35+1.65=2µJ

## Slide 11
Duty-cycle configuration delivery
  Why deliver Duty-cycle configuration in AMP trigger:
    The main contribution of Duty-cycle configuration is to allow Duty-cycle operation for trigger monitoring.
    The main behavior of AMP STAs is the monitoring of AMP trigger after wakeup.
    The trigger interval should be short in logistics like use cases, due to energy constraints and low latency requirement. It means AMP trigger is transmitted more frequently, which leads to easier detection for AMP STA after wakeup with less energy consumption.
  Why do not deliver Duty-cycle configuration in Beacon:
    Beacon is a parallel frame for AMP STA. It may have functionalities other than AMP trigger.
    Typical beacon interval is 100ms, which is too long for AMP STA to search after wakeup. It requires more energy consumption for initial beacon searching than that for trigger.
    If we consider short beacon interval, e.g. equal to trigger interval, the overhead and energy consumption will be equivalent for beacon and trigger.
    After detecting beacon, AMP STA still has to further receive trigger for UL PPDU transmission. Separate reception of Duty-cycle configuration and trigger brings additional complexity and energy consumption.
  Proposal:
    AMP STA can obtain Duty-cycle configuration through AMP trigger.
Chuanfeng He (OPPO)
Slide 11
Doc.: IEEE 802.11-25/0813r0
May 2025

## Slide 12
Summary and proposals
  In this submission, the details of Duty-cycle operation for AMP are discussed from power consumption perspective.
    With the assumptions on energy storage and power consumption model, it is feasible for AMP STA to support Duty-cycle operation for logistics like use cases.
    We try to identify some typical Duty-cycle operation parameters, such as duty cycle period, operation duration, in order to ease the further discussion on AMP TSF design.[6]
  To support Duty-cycle operation, it is proposed:
    Duty-cycle configuration is indicated through AMP trigger frame
      Duty-cycle configuration includes duty cycle parameters, e.g. duty-cycle period, service period length
    AMP STA or STA group specific Duty-cycle operation is supported to reduce collisions among AMP STAs’ accesses.
Chuanfeng He (OPPO)
Slide 12
Doc.: IEEE 802.11-25/0813r0
May 2025

## Slide 13
Straw Poll #1
Chuanfeng He (OPPO)
Slide 13
Doc.: IEEE 802.11-25/0813r0
May 2025
Do you agree with the following text:
  Duty-cycle configuration is carried in AMP trigger.
    Duty-cycle configuration includes duty cycle parameters, e.g. duty-cycle period, service period length.
Yes
No
Abstain

## Slide 14
Straw Poll #2
Chuanfeng He (OPPO)
Slide 14
Doc.: IEEE 802.11-25/0813r0
May 2025
Do you agree with the following text:
  AMP STA or STA group specific Duty-cycle operation is supported in 11bp.
Yes
No
Abstain

## Slide 15: Reference
IEEE 11-24/1500r0, Duty-cycle-amp-operation, OPPO
IEEE 11-24/1613r4, Specification framework for tgbp
IEEE 11-25/0341r0, Details of Duty cycle operation for AMP, OPPO
IEEE 11-23/2203r1, Updated technical report on support of AMP IoT devices in WLAN
IEEE 11-25/0285r1, SP Timing Synchronization with AMP Beacon, Huawei
IEEE 11-25/0814r0, Follow up on TSF for trigger based AMP, OPPO
Doc.: IEEE 802.11-25/0813r0
May 2025