## Slide 1: UL access mechanisms for Active Tx AMP STAs
Date: 2025-05-02
Authors:
Doc.: IEEE 802.11-25/0815r0
May 2025
Name | Affiliation | Address | Phone | Email
Chuanfeng He | OPPO |  |  | hechuanfeng@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Yinan Qi |  |  |  | v-qiyinan@oppo.com

## Slide 2: Background
The motions about UL access mechanisms for Active Tx non-AP AMP STAs were agreed.[1][2]
  MM-10: 802.11bp supports a time-slot based random access mechanism for Active Tx non-AP AMP STAs:
    AMP AP transmits an AMP frame that indicates one or more time-slots.
    Further details (e.g., frame formats, how a STA chooses a random access time-slot etc.) are TBD.
  MM-11: 802.11bp supports a time-slot based scheduled access mechanism for Active Tx non-AP AMP STAs:
    AMP AP transmits an AMP frame to assign one or more transmission time-slots.
    Further details (e.g., frame formats, how the time-slots are assigned etc.) are TBD.
Doc.: IEEE 802.11-25/0815r0
Chuanfeng He (OPPO)

## Slide 3
Time-slot based random access mechanism
  AMP AP transmits an AMP frame that indicates one or more time-slots for potential UL PPDU Tx without the request from AMP STAs.
  Random access mechanism is applicable to logistics like use cases
    AP has no knowledge of AMP STA’ ID.
    Small data is solicited by AP for AMP STA identification.
    Low latency is expected for fast AMP STA identification.
    Association is not required for one shot UL PPDU Tx from AMP STAs.
  Collision may happen in a time-slot with random access mechanism.
Chuanfeng He (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0815r0
May 2025

## Slide 4
Time-slot based scheduled access mechanism
  AMP AP transmits an AMP frame to assign one or more transmission time-slots for specific AMP STAs.
  Scheduled access mechanism is applicable to sensor like use cases
    Long term online and frequent UL data transmission.
    Association may be required, in which case AMP STA has AID for AP to assign time-slot.
  Collision can be avoided with scheduled access mechanism.
Chuanfeng He (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0815r0
May 2025

## Slide 5
Two phases time-slot based access mechanism
  Joint two phases access mechanism
    Random access phase: A AMP STA chooses one slot indicated by AMP trigger for random access (RA) signal transmission.
    Scheduled access phase: AP performs contention resolution based on the identified RA signals, and schedules slots for specific AMP STAs to perform data transmission.
  The RA signal is identified as temporary ID for AMP AP to assign time-slot for the AMP STA. The RA signal can be, for example:
    Random number, e.g. RN16
    CDM code, if CDM is supported for random access.
Chuanfeng He (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0815r0
May 2025

## Slide 6
Two phases time-slot based access mechanism
  Two phases access mechanism does not require the AID of AMP STA through association.
  Two phases access mechanism can avoid collision among UL data transmission during scheduled access phase, since temporary ID is identified during random access phase.
Chuanfeng He (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0815r0
May 2025
  Collison happens between AMP STA 3 and 4 during random access phase.
  Contention resolution by AP during scheduled access phase.

## Slide 7
One and two phases time-slot based access mechanism
  Standalone one phase access mechanism
    Time-slot based random access mechanism
      Random access for one shot and small data Tx.
      Do not require association.
      Typically for logistics like use cases.
    Time-slot based scheduled access mechanism
      Long term and frequent data Tx.
      Require AID through association.
      Typically for sensor like use cases.
  Joint two phases access mechanism
    Do not require association for AID.
    Random access for larger data Tx
    For collision sensitive access, e.g. access for larger data Tx, or heavy load access scenario.
Chuanfeng He (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0815r0
May 2025

## Slide 8
Proposal
  11bp supports standalone time-slot based random access mechanism and scheduled access mechanism.
  11bp supports joint two phases access mechanism, which includes random access phase and scheduled access phase.
  AMP AP transmits an AMP trigger frame that indicates the solicited type of access mechanism, and further the phase of two phases access mechanism.
Chuanfeng He (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0815r0
May 2025

## Slide 9
Straw Poll #1
Chuanfeng He (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0815r0
May 2025
Do you agree with the following text:
  802.11bp supports a time-slot based two phases access mechanism for Active Tx non-AP AMP STAs, which include:
    Random access phase: An AMP STA transmits random access signal through time-slot based random access mechanism.
    Scheduled access phase: An AMP STA transmits data through time-slot based scheduled access mechanism.
    Further details (e.g., random access signal, how a AMP STA chooses a access mechanism etc.) are TBD.
Yes
No
Abstain

## Slide 10: Reference
IEEE 802.11-24/1613r7, Specification framework for tgbp
IEEE 802.11-25/0334r1, Channel access for Active Tx non-AP AMP STAs – follow up, Huawei
Doc.: IEEE 802.11-25/0815r0
May 2025