## Slide 1: AMP Bi-static Backscatter in 2.4GHz
Date: 2025-05-10
Authors:
Name | Affiliation | Address | Email
Panpan Li | Huawei | Singapore | lipanpan25@huawei.com
Lei Huang |  | Singapore | 
Bin Qian |  | Shenzhen, China | 
Lumin Liu |  | Singapore | 

## Slide 2: Background
Motion 15: 11bp defines at least one mode of MAC/PHY that supports bi-static backscattering communication in 2.4 GHz.
[1] investigated UL coverage of bi-static backscatter. UL range of about 2 meter, may still be achieved when direct leakage is present for an DR of 50 dB with EH power levels that are relatively sufficient
This contribution intends to revisit the link budget analysis and answer following questions for both DL and UL
  Can bi-static reuse mono-static receivers?
  Can bi-static reuse mono-static Sync sequence?
AMP AP
AMP STA
Carrier
leakage
AMP Energizer
Backscatter signal

## Slide 3: DL Link budget (AP  STA)
Pr_STA (>=Rx sensitivity) = Pt_AP – PL(d)
Consider coverage 2m and STA Rx sensitivity -45dBm, AP Tx power need to be >=3.2dBm.
2.4GHz |  |  | 
Pt_AP (dBm) | 0 | 3.2 | 10
STA Rx sensitivity (dBm) | -45 | -45 | -45
DL distance(Friis channel) (m) | 1.8 | 2.6 | 5.6
DL distance (channel D) (m) | 1.4 | 2 | 4.4

## Slide 4: DL Assumptions
For mono-static backscatter, SNR at STA: -20-(-95)-10-9=56dB
For bi-static backscatter, SNR at STA: -36-(-95)-10-9=40dB
 |  | Mono-static | Bi-static
Coverage |  | 10-20cm | 2m
Tx power | Tx power | AP: 0dBm | AP: 10dBm
Receive signal modelling | Backscatter signal | 10cm PL: 20dB  -20dBm | 2m PL: 46dB  -36dBm
 | Rx noise | 80MHz thermal noise: -95dBm STA NF: 10 dB [2] Sensitivity of ~9dB for 100k ppm [2] | 
DL receiver | Detector | Non-coherent | 
 | Rx bandwidth | 80MHz | 
 | Rx sensitivity | -45dBm | 

## Slide 5: DL Assumptions
Data PER 10% @-3.3dB, PacketLen=80bits, ideal sync, 0ppm, L-LTF, Rx 2MHz
Mono-static SNR at STA: 56dB
Bi-static SNR at STA: 40dB
Bi-static backscatter may reuse mono-static backscatter DL receiver and Sync sequence.
May need to increase Tx power to achieve 2m coverage.

## Slide 6: UL Link budget (Energizer  STA)
Pr_STA (EH sensitivity) = Pt_E– PL(d)
The STA EH sensitivity limits the coverage from Energizer to STA
Consider coverage 2m, STA EH sensitivity need to be <=-28dBm.
2.4GHz |  |  |  | 
Pt_energizer (dBm) | 20 |  |  | 
STA EH sensitivity | -20 | -25 | -28 | -30
(Friis channel) (m) | 0.99 | 1.77 | 2.5 | 3.15
(channel D) (m) | 0.79 | 1.41 | 2 | 2.50
2.4GHz |  |  |  | 
Pt_energizer (dBm) | 20 |  |  | 
STA EH sensitivity | -20 | -25 | -28 | -30
 | 0.99 | 1.77 | 2.5 | 3.15
 | 0.79 | 1.41 | 2 | 2.50

## Slide 7: UL Link budget (STAAP)
AP
STA
Energizer
Signal:
Leakage:
Dynamic range: ~50dB
Noise
SNR
SNR = DR - (P_leakage - P_signal)
Pt_energizer (dBm) | 20 |  |  |  |  |  |  |  |  | 
backscatter loss (dB) | 5 |  |  |  |  |  |  |  |  | 
(m) | 2 |  |  |  |  |  |  |  |  | 
(m) | 1 |  |  |  |  | 2 |  |  |  | 
 | 60 | 90 | 120 | 150 | 180 | 60 | 90 | 120 | 150 | 180
SNR (dB) | 3.7 | 5.9 | 7.3 | 8.2 | 8.5 | -1.0 | 1.9 | 3.7 | 4.6 | 5.0
Pt_energizer (dBm) | 20 |  |  |  |  |  |  |  |  | 
backscatter loss (dB) | 5 |  |  |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  |  | 
 | 1 |  |  |  |  | 2 |  |  |  | 
 | 60 | 90 | 120 | 150 | 180 | 60 | 90 | 120 | 150 | 180
SNR (dB) | 3.7 | 5.9 | 7.3 | 8.2 | 8.5 | -1.0 | 1.9 | 3.7 | 4.6 | 5.0

## Slide 8: UL Assumptions
UL Performance for mono-static backscatter [4]
Bi-static backscatter may need a longer Sync than mono-static backscatter.
Bi-static backscatter may need better leakage removal.
Suggest keep clock restriction of bi-static backscattering same with mono-static: 100k ppm.
RxNF | Data rate | Clock accuracy | Rx power @10% SYNC+Data PER | SNR (dB)
-35dBr | 250kbps | 0ppm | -33 dBr | 2
 |  | 100kppm | -31.5 dBr | 3.5
 | 1Mbps | 0ppm | -26 dBr | 9
 |  | 100kppm | -22 dBr | 13

## Slide 9: Summary
For DL, bi-static backscatter may reuse mono-static backscatter receiver and Sync sequence.
For UL, bi-static backscatter may need a longer Sync than mono-static backscatter. Also, bi-static backscatter may need better leakage removal.

## Slide 10: Reference
[1] 11-25-0030-00-00bp-amp-ul-bi-static-leakage-and-dynamic-range-implications
[2] 11-24-1797-00-00bp-design-considerations-of-dl-data-rate-and-sync
[3] 11-24-1798-00-00bp-backscattering-ul-data-rate-and-modulation
[4] 11-25-0306-00-00bp-amp-backscattering-ppdu-and-sync-design