## Slide 1: Early Indication of RA-RU in DPS
Date: 2025-05-08
Authors:
Name | Affiliation | Address | Phone | Email
Ning Gao | OPPO |  |  | gaoning1@oppo.com
Liuming Lu |  |  |  | 
Chaoming Luo |  |  |  | 
Weijie Xu |  |  |  | 
Liangxiao Xin |  |  |  | 
Huixuan Zhou |  |  |  | 

## Slide 2: Introduction
The Dynamic Power Save (DPS) allows a DPS assisting STA to trigger the capability mode switching of DPS STAs with an ICF frame.
However, at the beginning of a TXOP, a DPS assisting AP may not able to address all necessary DPS non-AP STAs in a single ICF in case of aperiodic LL UL traffic of DPS non-AP STAs.
In baseline, AP is able to allocate one or more RA-RUs in trigger frames for non-AP STAs to transmit aperiodic UL traffic on-demand.
But in DPS, it would be very difficult for a DPS non-AP STA that is not addressed in the ICF to use these RA-RUs to transmit aperiodic LL UL traffic. Because the RA-RU may be outside of the operating BW of the low capability mode of this DPS non-AP STA.
In this contribution, we propose to use an early indication of RA-RU in the ICF to handle this problem.

## Slide 3: Proposed Method
A field in the ICF frame to indicates whether or not at least one subsequent Trigger frame with RA-RU is scheduled for transmission until the end of the TXOP in which the ICF frame carrying this field is sent.
  If yes, a DPS non-AP STA that is not address by the ICF may proactively switch its capability mode after the ICF and wait for the RA-RU in this TXOP.
  If not, a DPS non-AP STA that is not address by the ICF should keep low capability mode in this TXOP.
This early indication can help more DPS non-AP STAs proactively switch capability mode in order to transmit aperiodic LL UL traffic using RA-RUs.

## Slide 4: Summary
A problem of using RA-RUs to transmit aperiodic LL UL traffic in DPS is discussed in this contribution.
We propose to add an early indication in the ICF to indicate the existence of at least one subsequent trigger frame with RA-RU in this TXOP.
This indication can help DPS non-AP STAs that are not addressed by the ICF switch capability mode in advance so as to use RA-RUs to transmit aperiodic LL UL traffic quickly.

## Slide 5: SP 1
Do you agree to add a field into the ICF frame to indicates whether or not at least one subsequent Trigger frame with RA-RU is scheduled for transmission until the end of the TXOP in which the ICF frame carrying this field is sent ?
  Yes/No/Abstain