## Slide 1: Follow-up on CFO correction for COBF
Date: 2025-05-10
Authors:
Name | Affiliations | Address | Phone | email
Sameer Vermani | Qualcomm Technologies Inc. |  |  | svverman@qti.qualcomm.com
Alice Chen |  |  |  | 
Youhan Kim |  |  |  | 
Bin Tian |  |  |  | 
Ahmed Elsherief |  |  |  | 
Sherief Helwa |  |  |  | 
George Cherian |  |  |  | 
Meriam Rezk |  |  |  | 

## Slide 2: Introduction
In [1], we had proposed the CFO correction procedures for Coordinated beamforming (COBF)
  Several motions were adopted based on that proposal
In these slides we propose some modifications to the CFO correction procedure during the sounding stage, which harmonize the CFO correction between sounding and transmission stages
  We show that the new CFO correction procedure can work with various options of determining the sync reference/follower

## Slide 3: Reminder: Transmission stage CFO correction when Sharing AP is the Sync Follower
Sharing AP still transmits the COBF Trigger/Sync frame
Shared AP still aligns its frequency based on CFO estimate from the COBF Trigger/Sync frame
  No change in behavior at a shared AP in response to a COBF trigger/sync
The COBF Trigger/Sync and DL PPDU needs to be close in frequency to the sounding stage frequency of AP1
  Can be easily achieved through remembering the sounding stage pre-correction
Shared AP (AP2) estimates CFO w.r.t. sharing AP
Shared AP pre-compensates CFO before Tx
Sync-Follower AP
Sync-reference AP
Sync-follower AP is
TXOP owner
AP1
AP2
Transmitted with same pre-correction as sounding phase
DL PPDU
Sharing AP
DL PPDU
Shared AP
CoBF
Invite
SIFS
SIFS
CoBF
Response
SIFS
Shared TXOP
CoBF Trigger
/Sync
SIFS
STA1
STA2

## Slide 4: Key ideas: Transmission phase CFO correction
The AP that receives the sync frame always pre-corrects the COBF transmission that immediately follows
  Note that sync frame gives the recipient AP a CFO correction opportunity
  This is regardless of sync follower or sync reference designation
Follower AP remembers/maintains a pre-correction quantity
  When the follower AP is the sharing AP, while transmitting the sync frame and the subsequent COBF PPDU
    It pre-corrects based on the remembered pre-correction quantity (remembered from sounding stage or a recent sync frame reception)
When the reference AP is the sharing AP, while transmitting the sync frame or the COBF PPDU, no pre-correction is needed
  Reference AP does not remember any pre-corrections

## Slide 5: Note the following correspondence
For synchronization purpose we have following equivalence relation
  Cross-BSS NDPA during sounding stage == Sync Frame during transmission phase
  NDP transmitted in response to cross-BSS NDPA == COBF PPDU transmitted immediately after the sync frame
Note
  Each transmission TxOP can have a different sharing AP and shared AP
  Each sounding TxOP can have a different sounding initiator and responding AP

## Slide 6: CFO pre-correction during sounding phase: Learning from transmission phase
The AP that receives the cross-BSS NDPA frame always pre-corrects the NDP transmission that immediately follows
  Note that NDPA frame gives the recipient AP a CFO correction opportunity
  This is regardless of sync follower or sync reference designation
Follower AP remembers/maintains a pre-correction quantity
  When the follower AP is transmitting the cross-BSS NDPA frame and the subsequent joint NDP, it pre-corrects based on the remembered pre-correction quantity
When the reference AP is transmitting the cross-BSS NDPA frame or the subsequent joint NDP, no pre-correction is needed
  Reference AP does not remember any pre-corrections

## Slide 7: Pre-corrections needed for various frames
NDPAs transmitted by the reference AP
  No pre-correction needed
NDPAs transmitted by the follower AP for cross-BSS sounding
  Pre-correction needed based on most recent CFO estimate to the reference AP
    Either the last NDPA or a sync frame
    Just like COBF sync which always gets transmitted based on last remembered correction
Joint NDP transmitted by the follower AP, when the follower AP transmits NDPA
  Same pre-correction as NDPA
NDP in response to a cross-BSS NDPA (both joint and sequential sounding)
  The recipient of the NDPA always pre-corrects regardless of follower/reference designation
    This is like COBF Tx where the AP receiving the sync always pre-corrects

## Slide 8: Illustration when sounding process happens first in reference AP’s BSS
Sounding is happening first in reference AP’s BSS
NDPA
Reference
AP1
Follower
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
AP2 Calculates CFO and applies to NDP
AP1 Calculates CFO and applies to NDP
Uses most recent
pre-correction
Note: In the diagram, cross-BSS sounding happens first, and the reasons are shown in the appendix

## Slide 9: Illustration when sounding process happens first in follower AP’s BSS
Sounding is happening first in follower AP’s BSS
Reference
AP1
Follower
AP2
STA1
associated
with AP1
STA2
associated
with AP2
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
NDPA
NDP
CSI
BFRP
BF
RP
NDPA
NDP
CSI
Uses most recent
pre-correction
AP1 Calculates CFO and applies to NDP
AP2 Calculates CFO and applies to NDP
Note: In the diagram, cross-BSS sounding happens first, and the reasons are shown in the appendix

## Slide 10: Sync Reference/Sync Follower Determination
There are two options
  Sync reference determined during sounding-invite and sounding response exchange at the beginning of a sounding session
    The AP initiating the pre-sounding exchange in the first TxOP of a sounding session becomes the reference AP
  Sync reference determined at group formation
The CFO correction procedure shown in the slides works for both the options
Note: Sequence on slide 9 only happens for option 2

## Slide 11: Summary
We proposed a simple way to do CFO correction during sounding phase which is essentially analogous to transmission phase CFO correction
  Cross-BSS NDPA recipient always pre-corrects the next NDP regardless of reference/follower designation
  The follower AP when transmitting the NDPA uses the most recent pre-correction
    Either from a recent sync frame or a recent NDPA from reference AP
  NDPA transmitted by the reference AP never need to be pre-corrected
The design works well independent of how sync-reference and follower is determined

## Slide 12: SP1
Do you support that during the COBF sounding phase, cross-BSS NDPA recipient always pre-corrects the frequency of the NDP it transmits in response (pre-correction done based on the NDPA’s frequency estimate), regardless of reference/follower designation ?

## Slide 13: SP2
Do you support that during the COBF sounding phase, when transmitting the NDPA
  Reference AP does not perform pre-correction
  The follower AP should use a recent frequency pre-correction value for the CFO estimated to the reference AP

## Slide 14: References
[1] Document 11/25-0083r1, “CFO correction and related simplifications for COBF” Sameer Vermani (Qualcomm)

## Slide 15: Appendix
Sounding protocols

## Slide 16: Proposal: Cross-BSS sounding to happen first in sequential sounding
After a sounding initiation happens (sounding invite-sounding response exchange), it makes sense for the cross-BSS sounding to happen first due to the following reasons:
  The initiating AP that invited the other AP through a sounding AP shouldn’t do in-BSS sounding first while the responder AP is just a spectator on standby
    Invited the responder AP, better to give him involved after the invite
  The cross-BSS section of the sounding is bound to be more unreliable so it’s better to put that section upfront
    If that fails, in-BSS section may not be needed
  Also beneficial from the standpoint of ensuring full-rank-nulling
    An STA might reduce the NRx to be equal to Nc for cross-BSS sounding and then can maintain the same NRx for in-BSS sounding