## Slide 1: IMMW Idle Power Consumption
Date: 2025-05-12
Authors:

## Slide 2: Abstract
TGbn leverages multi-link operation and existing sub-7GHz MAC/PHY to provide non-standalone operation in 42~71 GHz band.
mmWave links are expected to have significantly higher idle power consumption due to higher frequency ADCs, beam training, and inherent characteristics of the mmWave devices.
In this contribution, we discuss options to reduce the idle power consumption of mmWave links.

## Slide 3: Idle Power consumption
As in [1], listening mode may contribute more than half of the power consumption of a modern device. This is the time when the device is awake but not transmitting or receiving.
For IMMW, a mmWave STA may need to be in listening mode when waiting to receive a frame from an AP (e.g. Beam training frames, DL Data/control frames, etc.)
To allow the mmWave STA to conserve its power while listening, we can leverage the ICF/ICR exchange in 11bn.

## Slide 4: Dynamic Power Save in 11bn
The DPS operation allows a DPS STA to operate in a lower capability (LC) mode and to transition to higher
capability (HC) mode upon reception of an ICF transmitted by its AP. The DPS STA in higher capability (HC) mode transitions back to the LC mode after communication with the AP.
Lower capability mode
SIFS
Higher capability state
Transition delay
ICR
AP
DPS STA
ICF
pad
F
C
S

## Slide 5: Minimum Bandwidth for IMMW STAs
In [2-3], minimum bandwidths of 80 MHz and 160 MHz were considered. Since decoding ICF frames is required for DPS, it means that a mmWave STA is required to be always ready to receive an 80 MHz or 160 MHz control frame.
This may result in an idle power consumption in mmWave to be much higher compared to sub-7GHz STA in lower capability mode.
- ADCs for 20 MHz vs 160 MHz can have about 8x more power consumption.

## Slide 6: Possible Approaches
ICF transmit/receive similar to 11bn but done at 80/160 MHz.
  High idle power consumption but design is simple.
20 MHz RSSI based listening (no decoding)
  Option 1 –ICF is transmitted using 80/160 MHz.
  Option 2 – ICF is transmitted using 20 MHz.
  Possible false alarms due to interference.
  Low idle power consumption.
3. Cross-link ICF
  In this method, the ICF for the mmWave link is transmitted in a sub-7GHz link
  Disadvantage: potential congestion problems in the sub-7GHz link.

## Slide 7: Conclusion
We discussed the need for reducing the idle power consumption for IMMW STAs. Due to the much higher base bandwidth, listening operation by mmWave STAs may be much higher any may result in faster battery drain of IMMW enabled devices.
We proposed several approaches to reduce the idle power consumption.

## Slide 8: References
[1] https://mentor.ieee.org/802.11/dcn/22/11-22-1414-01-0uhr-low-power-listening-mode.pptx
[2] https://mentor.ieee.org/802.11/dcn/25/11-25-0854-00-00bq-considerations-on-numerology-for-immw.pptx
[3] https://mentor.ieee.org/802.11/dcn/25/11-25-0360-00-00bq-high-level-thoughts-on-immw-phy-design.pptx
[4] https://mentor.ieee.org/802.11/dcn/24/11-24-0471-00-immw-considerations-on-power-consumption.pptx

## Slide 9: SP
Do you agree that power consumption of mmWave STAs during listening should be made similar to sub-7ghz STAs.