## Slide 1: 802.16/802.24 Tutorial: Proposed 802.16s Narrowband Project 802.24 Vertical Applications TAG - applications of 802.16 in utility field area networks
Tim Godfrey (EPRI)

## Slide 2: Agenda
What is a Field Area Network (FAN)?
Why would a utility use 802.16? Why not LTE?
What are spectrum options for FAN?
Why amend 802.16?

## Slide 3
Core
Fiber
Private Field Area Network
Collector
Commercial Cellular Network
Collector
Sensor
Cap Bank
LAN
WAN
FAN
NAN
Microwave
Cap Bank
PV
Premises

## Slide 4: Utility Deployed FAN – private network
Simplified chart – many other factors must be considered
Licensed Spectrum Available?
No
Yes
Paired (FDD) Spectrum?
Yes
No
802.16 WiMAX
Unlicensed Mesh
LTE
Large Coverage Area?
Yes
No
Unlicensed P-P

## Slide 5: Popular 802.16 products for utilities
GE MDS Mercury 3650
Siemens
RUGGEDCOM WIN7200
Airspan AirSynergy 4G
Full Spectrum FullMAX
Cisco Connected Grid
Router (Station Only)

## Slide 6: LTE Network Architecture
Fully integrated with legacy mobile system
Oriented towards mobile network operators needs
Notes: MME Mobility Management Entity
PLMN: Public Land Mobile Network
SGSN: Serving GPRS Support Node
HSS Home Subscriber Server
PCRF: Policy and Charging Rules Function
PDG: Packet Data Gateway

## Slide 7: 802.16 Network Architecture
Simpler architecture with L2 support
More aligned with utility IT services and architecture
Optional
Notes: http://www.tutorialspoint.com/wimax/wimax_network_model.htm

## Slide 8: Other key differences in 4G technologies
Spectrum Type
  LTE typically uses FDD (paired) spectrum,
    TD-LTE standard does support unpaired
    Most equipment is for FDD
  WiMAX typically operates in unpaired spectrum
    Best match to “uplink biased” grid applications
IEEE 802 Ethernet Model
  Intrinsic support for Layer 2 connectivity
  IEEE 802.16 supports an Ethernet Interface and Layer-2 messages (e.g. IEC 61850 GOOSE)
  LTE is IP (layer 3) only – Layer 2 must be tunneled
Local forwarding
  802.16 supports direct SS to SS forwarding through base station
  LTE typically routes all packets through EPC
    Local gateways have been proposed
DL Freq
UL Freq
Time
Frequency
DL
UL
Time
DL
UL
FDD
TDD
ASN GW
EPC

## Slide 9: Why not Cellular IoT or other commercial wireless?
Public
Low CapEx, ongoing OpEx
Security and reliability up to carrier
Carrier provides the spectrum
Network evolution up to carrier
Network maint & repair up to carrier
Private
High CapEx, lower OpEx
Utility controls security and reliability
Utility provides the spectrum
Utility controls pace of evolution
Utility controls maint & repair
Utilities that choose the private option have specific financial and operational reasons, and are unlikely to change to a public provider.
They are not potential customer for operators

## Slide 10: Spectrum for utility 802.16 FANs
5.8 GHz Unlicensed
  WiMAX certification and profiles
  Less attractive due to poor propagation at high frequency
4.9 GHz Public Safety
  WiMAX certification and profiles
  Limited availability of spectrum – negotiation with PS entities required.
3.65 GHz “Lightly Licensed”
  WiMAX certification and profiles
  Has been widely used by over 100 utilities.
  Recent rules changes have made the band less attractive for future expansion
  Reports of interference in utility pilots
1.8 GHz Canadian band
  WiMAX certification and profiles
  Widely used Canadian utilities.
700 MHz Upper A Block
  Superior propagation
  Too narrow to support 802.16 or LTE as currently specified

## Slide 11: Why narrow channel is of interest
Spectrum is less attractive to mobile operators since LTE is not supported
  Cost is moderated
Narrow spectrum means lower data rate, but capacity is still sufficient for grid applications
Other spectrum with similar narrow channel characteristics is available or may become available:
  217 MHz, 406 MHz, 901 MHz, 1.4 GHz

## Slide 12: Conclusion
802.16 is technically well suited for utility Field Area Networks
802.16 continues to be widely used for utility Field Area Networks
The industry desires to use 802.16 for 700 MHz and in other narrow allocations, but a standard is needed