## Slide 1: TUTORIAL (20)
Security:
A dedicated VLAN sidesteps some of the issues associated with security.
Providing location information is forbidden in some countries, mandatory in others.
Provided location information is considered to be sensitive information.
Information integrity across the call is a security issue.
Information needed for call back is considered to be sensitive.
The actual content of the call may be considered to be sensitive.

## Slide 2: TUTORIAL (21)
Security (2):
The security considerations for ECRIT are put forth in IETF RFC-5069
There are a few problems which seem to be intractable in a wireless environment with unauthenticated users.
Originating call location information from unauthenticated users will be visible (“Hollywood Paparazzi Problem”) unless we encrypt (at least) the over-the-air portion of those calls.
  We believe that the current population of public access points has no way to provide encryption for unauthenticated users.
  We believe that the current population of 802.11 access points has no way to preserve security while switching SSIDs (for further investigation).

## Slide 3: TUTORIAL (22)
Security (3):
First hop encryption is a significant challenge.
First hop encryption will possibly require changes from the wireless MAC groups.
First hop encryption should not be allowed to delay work on the primary functionality of “getting the call through”.

## Slide 4
IEEE 802 MAC
Call origination
Upper Layer Client
(presumably IP)
Call destination
Upper Layer Client
(1st Router)
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
Location
Determination
Reconciliation
Sub-Layer
IEEE 802 EMERGENCY SERVICES ARCHITECTURE RE: Location Determination
Air
Air, wire or fiber
IEEE 802 MAC
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
Relay Sub-Layer
Location
Determination
Reconciliation
Sub-Layer
Location
Determination
Reconciliation
Sub-Layer
IEEE 802 PHY
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 MAC
Relay Sub-Layer
Location
Determination
Reconciliation
Sub-Layer
Location
Ranging
Module & MIB
802 → ECRIT Handover
Reconciliation
Sub-Layer
1st Access point for
Wireless instance

## Slide 5
IEEE 802 MAC
Call origination
Upper Layer Client
(presumably IP)
Call destination
Upper Layer Client
(1st Router)
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
Relay Sub-Layer
Location
Determination
Reconciliation
Sub-Layer
IEEE 802 EMERGENCY SERVICES ARCHITECTURE re: Location Determination
Wire or fiber
Air, wire or fiber
Location
Determination
Reconciliation
Sub-Layer
Generic relay point
Assume for the time being that network to the right side of the line is:
a) Not dynamic
b) Secure on a hop by hop basis
802 involvement ends at the 1st router when the frame is separated from the SA/DA & Type fields

## Slide 6: Issues
U.S. Government preference is for infrastructure based location over that from end station based location information. (GPS reliability in cities and inside buildings is a problem, as is spoofing.)
802.16 distance and angle measurement is not of sufficient accuracy to meet the requirements E911 & NG911.
802.11 service leaking into adjacent properties is a well known problem for which we have no solution. That is, being able to provide accurate street address information of the caller.

## Slide 7: Issues (2)
This is all a contentious technical area, both from a feature/content point-of-view and from a division of work/layer/SDO assignment point-of-view.
Just what are the regulatory requirements (from around the world)?
What technical work needs to be done first/now? (We can't just wait until everything is written in stone to start.)
What pieces will get done:
  in what layer?
  In what SDO?
Getting good answers to all of this is the first task for the group.

## Slide 8: BACKUP SLIDES

## Slide 9: Call sequence via wireless end link 802.11 not 802.16 How to fix?
AP->Sta Beacon of SSID for ES VLAN
STA picks a beacon
STA sends “Authenticate request”
AP sends “Authenticate reply”
STA send “Associate request”
AP sends “Authenticate reply”
STA sends DHCP request
AP passes back DHCP response
  DHCP response contains IP address for station, gateway IP address.
STA send ARP request with Gateway IP addr to get Gateway DA
AP passes back ARP response from Gateway with its DA
STA can now communicate directly to Gateway via IP

## Slide 10: Call sequence via wireless end link
STA sends ES SIP Request to Gateway
(Is location information sent at this point or in subsequent packets)?
About now, 802 has pretty much set up its job except when the time comes for Call-Back. (Handover and roaming problems excluded)
Advance information query can come back after call is established.
We need to say more about roaming and handover. Much study needed in multiple WGs.

## Slide 11
IEEE 802 MAC
Call origination
Upper Layer Client
(presumably IP)
Call destination
Upper Layer Client
(1st Router)
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
IEEE 802 MAC
IEEE 802 PHY
Relay Sub-Layer
Location
Determination
Reconciliation
Sub-Layer
Location
Determination
Reconciliation
Sub-Layer
IEEE 802 EMERGENCY SERVICES ARCHITECTURE RE: Location Determination
Air
Air, wire or fiber
Location
Ranging
Module & MIB
1st Access point for Wireless instance