## Slide 1: TUTORIAL (11)
What we believe 802 needs to finish the task:
Specific referenced external req'ts from ECRIT
Specific interface specs from ECRIT harmonized and reconciled to our requirements
Agreement within various 802 W.G.s to tweak their pieces.
An ES WG to generate a single standard to reconcile the upper layer interface.

## Slide 2: TUTORIAL (12)
What we believe 802 may offer to improve the solution:
A standard that includes means to:
Provide end & perhaps per hop location in 802 networks.
Give emergency calls priority in 802 networks ?
Provide information to enable Callback
Provide a LOCAL connection mechanism (e.g. bypass various tunneling schemes)
Provide service to unauthenticated users to a default VoIP router.
Spoofing and security are issues

## Slide 3: TUTORIAL (13)
IN SHORT:
ES-ECSG intends to provide what ECRIT needs.
We will work with ECRIT to provide optimal solutions.

## Slide 4: TUTORIAL (14)
Possible technical concepts:
Provide end location in 802 networks.
  802 ES to provide/harmonize end station location MIB to ECRIT format requirements.
Provide per-hop location in 802 networks.
  Adapt/use existing mechanism from 802.1ag and equivalents from 802.11.

## Slide 5: TUTORIAL (15)
Possible technical concepts:
Give emergency calls priority in 802 networks.
  Use existing priority mechanisms in 802.1Q
  NOTE: Priority access or call handling is not a current requirement in 112/911 systems nor anticipated in the remainder of VoIP systems.

## Slide 6: TUTORIAL (16)
Possible technical concepts:
Provide information to enable Callback.
  Provide both originating terminal location MIB information and per-hop network information as part of session initiation information to the network attachment router.
  This would provide “hints” that the 802 network could use if call is disconnected and straightforward callback turns out to be a problem.

## Slide 7: TUTORIAL (17)
Possible technical concepts:
Provide a LOCAL connection mechanism (e.g. bypass various tunneling schemes).
  Provide a VLAN (or equivalent) across all 802 networks that is dedicated exclusively to Emergency Services. It would have a single destination, i.e. the network attachment router.
  We anticipate that packets will be steered to this new dedicated VLAN by the use of a new EtherType.

## Slide 8: TUTORIAL (18)
Possible technical concepts:
Provide service to unauthenticated users.
  This could be difficult, but is a firm regulatory requirement in cellular systems. (Not required in VoIP?)
  We believe a dedicated VLAN will make it easier than it would be to do otherwise.
  No authentication would be needed to use the dedicated VLAN, but it can only be used to get to the PSAP.

## Slide 9: TUTORIAL (19)
Spoofing:
End and per-hop location information as provided will be available as a tool for use in dealing with this classical problem.