## Slide 1: 2/4/2010 Con Call output
This version is Geoff's edits as taken in the conference call.
It includes implementation of the editing instructions talked about in the 1/29 conference call
Further edits through Feb 4 11:00 AM, 2010 Geoff Thompson
Edits during conference call Feb 4, 2010 2:00 PM – 3:37 PM by Geoff Thompson
Further Edits by Geoff Thompson in prep for Con Call 2:00 PM PST Feb 11, 2010
Further Edits by Geoff Thompson since posted version and in prep for Con Call 2:00 PM PST Feb 17, 2010

## Slide 2: 802 EMERGENCY SERVICES TUTORIAL
Why 802 needs an Emergency Services Project and what we think it should look like.
802 ES-ECSG
Geoff Thompson/InterDigital Scott Henderson/RIM
Others from .16 (Barber) & .11?

## Slide 3: Agenda New
Break up in to separate presentations and presenters
Who will present for ES and how will the tutorial be broken into presenters?
  Presenter 1/Topic
  Presenter 2/Topic
Presenting for 802.11?
Presenting for 802.16 - Phil Barber
Presenting for 802.1?

## Slide 4: Agenda New
Introduction
Presenting for 802.11?
Presenting for 802.16 - Phil Barber
Emergency Services EC Study Group
  Presenter 1/Topic
  Presenter 2/Topic
Wrap up
  Q & A
  Straw Polls

## Slide 5: Technical/Regulatory Problem Statement
(US Historical Case) 911 Call Origination Identification: Originally based on the wireline legacy incumbent local exchange carriers' databases of their customers.
The legacy system in its original form was seriously compromised as:
  Local phone service ceased to be dominated by a wireline monopoly.
  Cellular phones became significant. (They had no built-in location mechanism. They also had a weakened sense of just where they wanted to call for 911.)
  VoIP phone services grew. VoIP has no inherent caller or call target physical location knowledge.
  Wireless inherent authentication was weakened.

## Slide 6: Regulatory Technical Problem Statement
Emergency Services calls need:
To be directed to the appropriate PSAP
Carry originating location information
To provide sufficient information for PSAP call-back
Further (possible future but not current):
Systems are required to provide service to any user. (Authorized subscriber or not) some countries
Some prioritization capability should be considered
Notes: Per RFC 5012
Location (civic or geographic) is required for two separate purposes:
- To support routing to appropriate PSAP
- To display the caller’s location to the call taker
- (Emergency Service Number) What layer?
(i.e. “visited emergency dial string”)
- (Servicing PSAP) What layer?
Support "Infrastructure Based Emergency Call Routing” Ref: RFC 5012 4.7 7. For infrastructure-based emergency call routing (in contrast to UE-based emergency call routing),
the emergency call routing support entity needs to forward the call to the PSAP.
- Infrastructure based location data
- Infrastucture based:
Determination of appropriate PSAP
Routing to PSAP

## Slide 7: FCC Consumer Info Sheet
http://www.fcc.gov/cgb/consumerfacts/voip911.pdf

## Slide 8: (Example:) US Requirement (adapted from: www.fcc.gov / cgb / consumerfacts / voip911.pdf
The US FCC has imposed the following requirement:
All interconnected VoIP providers must automatically provide 911 service to all their customers as a standard, mandatory feature without customers having to specifically request this service. VoIP providers may not allow their customers to “opt-out” of 911 service.

## Slide 9: Requirements: Other countries
Other countries have similar requirements.
There are national differences, especially with respect to:
  Emergency numbers other than “911”.
  See: http://www.sccfd.org/travel.html.
  Some countries have several numbers
  Some countries prohibit location info.
  Other details

## Slide 10: Defined Problem lies in Multiple Domains
IP, routing and higher layer portions of the problem belong to the IETF.
These problems are being addressed primarily by IETF ECRIT.
The below Layer 3 portion of the problem is for 802 to address.
802.11 and 802.16 have already done some explicit work in this area.
Needs to be handled uniformly across 802.

## Slide 11: 802 Problem
IEEE 802 needs a single standard so that IP applications “should” not need to know which 802 MAC is currently being used.
This is envisioned as a “shim layer” that goes between an 802 end station MAC and its upper layer client.
There may be similar pieces required for 802.1 relays to add per-hop location information (may be required for location back-up information when no end-location information is provided).

## Slide 12: “Complex Problem?”
SUPPORT OF EMERGENCY SERVICES and THEIR (present and future) REQUIREMENTS FOR PACKET NETWORKS IS A HUGE, COMPLEX PROBLEM FOR WHICH THE PROBLEM ITSELF IS NOT YET FULLY DEFINED. A successful Emergency Call depends on all layers of the network
For our proposed scope we feel that the problem is fully defined.

## Slide 13: “Complex Problem?”
SUPPORT for the full scope of EMERGENCY SERVICES and THEIR (present and future) REGULATORY REQUIREMENTS FOR PACKET NETWORKS IS A HUGE, COMPLEX PROBLEM FOR WHICH THE PROBLEM ITSELF IS NOT YET FULLY DEFINED.
The scope for this project is much smaller and well defined i.e.: Only support VoIP citizen-to-authority calls.

## Slide 14: How Complex ?
There are pieces of the ES problem that:
Are well defined today
Have existing regulatory (or derivative) requirements
Are not addressed across 802.

## Slide 15: TUTORIAL (4) LOCATION
The biggest piece:
802 originated (and VoIP originated) “calls” to the PSTN don't carry the information required (e.g. location) for emergency calls (There are proprietary exceptions)
There are uncoordinated pieces within some WGs.
There are existing IETF requirements for these ES calls that are not being met.

## Slide 16: TUTORIAL (6) More about Location
Why VoIP doesn't work for ES calls today:
The Internet was designed to be “location neutral”.
Traditional “112/911” was designed around and serviced by a localized static wired infrastructure (end office circuit switched systems)
VoIP services are highly decentralized and often cross national boundaries (regulatory problem)

## Slide 17: TUTORIAL (7) More about Location (2)
Why VoIP doesn't work today (cont'd):
Today, the VoIP service provider has no knowledge of the caller's location within the Internet (almost true).
A PSAP has no prior knowledge that a caller is within their service area.
Therefore, associating caller and proper PSAP is a big problem
VoIP service providers are not sufficiently regulated to fully handle the ES problem; there are significant technical, geopolitical and legal jurisdiction problems involved (language too).

## Slide 18: TUTORIAL (8) IETF & Emergency Services
The IETF – ECRIT group has taken on the task of solving this problem for the upper layers.
See: ietf.org/dyn/wg/charter/ecrit-charter.html
7 Internet drafts, 7 RFCs
Includes “Requirements”, “Framework” and “Best Current Practices”
See also R. Barnes/Hannes Tschofenig IETF preso: geopriv.dreamhosters.com/esw6/PEACE-Vortrag_v5.ppt

## Slide 19: TUTORIAL (9) ECRIT
The IETF – ECRIT group has taken on the task of solving this problem for the upper layers.
802 needs to liaise with ECRIT to
Provide a complete solution that encompasses 802 end networks.
Agree precisely on requirements from 802
The solution should look the same to ECRIT without regard to which 802 technology is in use.

## Slide 20: TUTORIAL (10) ECRIT (2)
What does ECRIT need from 802 to meet these requirements?
What can IEEE 802 provide to ECRIT to meet these requirements?
Provide location of and/or to end station.
Offer Layer 1 & 2 element location information
Spoofing and security are issues
Prefer LOCAL connection (e.g. bypass various tunneling schemes)
Provide service to unauthenticated user (Initiate & handover/callback)