## Slide 1: IEEE 1900 New Project Proposal Spectrum Consumption Modeling
Slide 1
Date: 2012-06-25; Grenoble, France
Authors:

## Slide 2: Motivation
The advanced radio community is in need of standard ways to compute coexistence and to convey policy to radios
The regulatory community is in need of means to manage sharing of spectrum and to specifying spectrum usage rights
The commercial spectrum management community (i.e., whitespace database administrators) are in need of a means to specify quanta of spectrum for trading
Operational communities are in need of a means to manage spectrum dynamically
Model-Based Spectrum Management (MBSM) provides a solution that addresses all of these needs
MBSM can be standardized and the DySPAN-SC is the best forum for this effort

## Slide 3: Abstract
Slide 3
Spectrum Consumption Models (SCM) capture the boundaries of spectrum uses for objective arbitration of compatibility
  SCM integrate spectrum management and DSA policy creation
  SCMs are machine readable and will enable technologist to develop RF systems that can receive spectrum policy guidance dynamically
  SCM can support the trading and sharing of spectrum
MBSM will enable a comprehensive DSA enterprise
  Technology – SCM can convey spectrum assignments and spectrum policy to RF systems and be used for M2M coordination of spectrum use
  Commerce – They capture the quanta of spectrum that are traded
  Regulation – They can define a user’s spectrum usage rights
  Operations – They enable dynamic and flexible management and sharing
Based on the anticipated benefits of MBSM, I propose that the IEEE DySPAN-SC form a Study Group to write a Project Authorization Request (PAR) to standardize SCM
25/06/2012

## Slide 4: The DSA Enterprise
Spectrum
MBSM is the catalyst of the enterprise and bridges the needs of the different communities
Regulators
Federal users
Commercial users
Technology developers
Unlicensed users
Brokers

## Slide 5: Model-Based Spectrum Management
Spectrum management (SM) based on the creation and exchange of spectrum consumption models (SCMs)
  SCMs capture the consumption of spectrum identifying the boundaries of spectrum use, not the details of systems
  SCMs have attendant computations for assessing compatibility among models (A common means across the entire SM system)
  SCMs are a loose coupler for the spectrum enterprise
    The minimal amount of data at the intersection of the activities of SM
    Captures the intent of users and the judgment of spectrum managers
    Conveys spectrum use policy
Enables sharing of spectrum and spectrum markets

## Slide 6: What is a loose coupler?
A thing that exists at the intersection of a large set of systems that allow them to interoperate and to be integrated
A key component of innovation and composable capabilities
  Layers enable local innovation
  Loose couplers enable integration
  Bowties enable composability
Loose Coupler
Innovation
Innovation
Layer
Layer
Bowtie
Layer
Layer
Interface
Diversity
Diversity

## Slide 7: Well known examples of loose coupling
Benefits
  Integration
  Interoperability
  Innovation
60 Hz AC
Power Producers
Power Users
IP
Datalink Technologies
Applications
Innovation
Composability
Standard
Composability
Innovation

## Slide 8: Spectrum Consumption Modeling as a Loose Coupler

## Slide 9: We have published a first draft on modeling
The “Modeling and Computation Manual” is a first attempt to create a standard and is available on-line at http://www.mitre.org/work/tech_papers/2011/11-2071/
Exposed to the DySPAN community at conferences and through email
Currently updating this first draft based on feedback

## Slide 10: Thirteen SCM modeling constructs
Total power
Spectrum mask
Underlay mask
Power map
Propagation map
Intermodulation masks
Platform
Location
Start time
End time
Minimum power
Protocol or policy
Probability
Not collected as data about a system but used to build a model of a system’s spectrum use
Captures the spectral content of the signal and the unique characteristics of spread spectrum systems
Can capture antenna effects
Can capture behaviors that enable compatible reuse
Can capture environmental effects
Captures susceptibility to intermodulation
Enable greater resolution in spectrum management
Captures the uncertainty in the model constructs

## Slide 11: Combining Constructs into Models
Transmitter _______ _______ _______ _______
Receiver _______ _______ _______ _______
System _______ _______ _______ _______
Transmitter_1
Transmitter_2

Transmitter_n
Receiver_1
Receiver_2

Receiver_m
End of System
Collection _______ _______ _______ _______
System_1
System_2

System_i
Transmitter_1
Transmitter_2

Transmitter_j
Receiver_1
Receiver_2

Receiver_k
End of Collection
Modeling constructs are found in transmitter and receiver models and in system and collection headings
Constructs define emissions
Constructs define interference
Proposal provides an XML schema for this type of model construction

## Slide 12: Building Models
System Model
  Constructs in heading define the boundaries of system operation
  Lists transmitter and receiver models with more limiting constructs
Collective Consumption Listing
  Constructs in heading define the limits to which the collection is complete
  Lists systems, transmitters and receivers of spectrum consumers that consume spectrum within the limits of the collection
Spectrum Authorization Listing
  Constructs in the heading define the limits of the overall authorization
  The lists of system, transmitter, and receiver models identify available spectrum
Spectrum Constraint Listing
  Constructs in the heading define the limits of the collection of constraints
  The lists of system, transmitter, and receiver models identify existing uses of spectrum that have precedence

## Slide 13: Why model spectrum use?
Captures and allows sharing of judgment
Enables distribution of the spectrum management problem
Changes nature of spectrum management
  From seeking persistent solutions to one seeking dynamic solutions
  Greater spatial and temporal resolution
Enables creation of algorithms for improved spectrum management
  Assessing compatibility of uses
  Automation of channel assignment
  Searching for suitable spectrum
Supports Policy-Based Spectrum Management and Dynamic Spectrum Access
  Models are policy
  Models are machine readable
  Provides means to manage DSA systems
Conceals sensitive details of equipment and its use while still revealing spectrum consumption for spectrum management tasks

## Slide 14: What are the desired characteristics of modeling?
Provides a means to capture consumption
  Emission of radiation by transmitters
  Susceptibility to interference at receivers
  Propagation effects
  Directivity of gain
  Time and location of use
Simple common means to compute compatibility
Supports the development of tractable algorithms
Independent of external data (e.g., terrain databases)

## Slide 15: Drivers of the Business Case
The requirement to share spectrum
  Incumbents cannot move
    Too costly
    Impractical to create similar capabilities in other bands
  Diverse uses that must be made compatible
  Sensitivity on revealing how spectrum is used
The evolution of a commercial model for brokering spectrum (e.g., TVWS)
The development of dynamic spectrum access radios (e.g., whitespace devices) and networks

## Slide 16: The business of spectrum sharing
Spectrum Market
Spectrum owners work with a database administrator to model spectrum they can share
Models of available spectrum are shared across the spectrum market
Database administrators work as brokers arbitrating the lease of spectrum and collecting commissions for the service
Spectrum Owner
Database Administrator
Database Administrator
Customer
Database Administrator
Database Administrator
Database Administrator
Customer
Customer
Customer
Customer

## Slide 17: A standard for spectrum consumption modeling solves critical challenges
Challenge | Solutions
Sensitivity of incumbent use | Modeling is abstract and artful. It is possible to reveal spectrum availability without revealing existing uses
Managing coexistence | Models have attendant computation for compatibility. Once modeled, methods of computing compatibility are the same throughout the system
Enforcement | Models convey the boundaries of use. Arbitration of interference would be objectively based on adherence to those boundaries
Responsiveness | With models, algorithms can be created to perform hard spectrum management tasks: searching for available spectrum, optimizing assignments, managing spectrum access

## Slide 18: How modeling would change spectrum management
Data
Judgment
Tools
Decision
Data
Judgment & Intent
Tools
Models
Tools
Decision
The judgment of the spectrum manager is lost after the decision is made
The judgment of the spectrum manager and the intent of the user is embedded in the model
The models enable algorithms to perform hard spectrum management tasks
Today
With Spectrum Consumption Modeling

## Slide 19: How Would SCM Change Spectrum Management
Spectrum management can be made more dynamic and more effective
  Supported by automation
  Assignments can be made at the operational levels closer to the user
Spectrum management activities can be distributed
  Integration of regulatory and commercial activities
  Collaboration and communication among different commercial agents

## Slide 20: How Would SCM Help Regulators
Regulators can define spectrum usage rights with models
Data
Judgment & Intent
Tools
Models
Tools
Decision
The judgment of the spectrum manager and the intent of the user is embedded in the model
The models enable algorithms to perform hard spectrum management tasks
With Spectrum Consumption Modeling

## Slide 21: How would SCM enable technology development
Models serve as a loose coupler in spectrum management and would serve as a catalyst for innovation
  In management
  In policy creation
  In M2M collaboration

## Slide 22: What would the proposed standard include
A definition of the constructs used to model spectrum use
A definition of the methods to compute the compatibility among models
P1900.2
Provides elements of a policy ontology for P1900.5.1

## Slide 23: Recommendation
Establish a study group to explore the development of a PAR for this effort

## Slide 24: Poll
The IEEE DySPAN SC should establish a Study Group to propose a PAR for Spectrum Consumption Modeling
  Yes
  No
  Abstain