## Slide 1
IEEE 802 OmniRAN Recommended Practice ToC Proposal |  |  | 
Date: 2013-09-16 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Yonggang Fang | ZTE |  | yfang@ztetx.com
Bo Sun | ZTE |  | sun.bo1@zte.com.cn
Kaiying Lv | ZTE |  | lv.kaiying@zte.com.cn
ZhiQiang Han | ZTE |  | han.zhiqiang@zte.com.cn
Notice: This document represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on contributors, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This contribution proposes ToC for Recommended Practice document of omniRAN.

## Slide 2: Recommended Practice ToC
IEEE 802 OmniRAN Architecture

## Slide 3: Background
Recommended Practice
  OmniRAN project was approved to develop a Recommended Practice document [1]
  Draft ToC of the Recommended Practice was proposed in [2]
  [3] suggests omniRAN architecture model to cover
    Cellular offload in hotspot [4] [5]
    SDN used to manage backhaul network to multiple service networks in access network sharing [6]
    SDR used to self-configure and optimize radio access network such as [7]
      ZigBee SEP2 networks
      WLAN
This contribution proposes updated ToC.

## Slide 4: OmniRAN Recommended Practice ToC
Introduction and Scope
Abbreviations, Acronyms, Definitions, and Conventions
References
Identifiers
Tenets for IEEE 802 OmniRAN Systems
Network Reference Model
  Overview
  OmniRAN Architecture
    Network Entity Descriptions
    Reference Points
Functional Design and Decomposition
  OmniRAN Initialization
  OmniRAN Admission Control
  Connection Establishment
    Network Discovery and Selection
    Association and De-association
    Authentication and Authorization
    Datapath establishment, switching, and teardown
    QoS and policy control
  Accounting

## Slide 5: OmniRAN Architecture
Separate planes
  Data Plane Functionalities:
    carrying, sequencing, tunneling, forwarding the user data traffic between the Core network, AN and Stations
  Control Plane Functionalities:
    service management, user traffic connection setup, mobility management, accounting management, etc.
  Management Plane Functionalities
    carrying signals used for authenticating, controlling and managing the OmniRAN infrastructure (AP); and support configuration for SDR/SDN.
Why need separate planes
  Different plane ends at different network entity
    R3-D is the Reference Point between AP and SDN (backhaul),
    R3-C is the Reference Point between AP and SDN controller.
  Different plane may have different protocol stacks
    R3-D is mapped to GTP-U in the cellular offload use case
    R3-C is mapped to GTP-C in the cellular offload use case

## Slide 6: OmniRAN Architecture
Station
Internet
Core Network(s)
Core
Operator C
RAN
SDN
(backhaul)
SDN
Controller
Data path
Control/Management path
Access Abstraction
Access Abstraction
R1
R3-D
Core
Operator B
Core
Operator A
Access Abstraction
R4-D
R5
R5
Access Abstraction
Backhaul Abstraction
AP1
AP2
AP1
R3-C/R3-M
R4-C
R2

## Slide 7: OmniRAN Reference Points
Reference Points denote the interconnections between functional entities of access network, i.e.:
  R1 between station and access network:
    Access link, technology specific
    Remote configuration/management mechanisms for 802 radio links, including station and access points; User plane management of the multiple-interfaced stations;
  R2 between station and core network:
    User & device authentication, subscription & device management
  R3 between the access network and the core network:
    R3-M: support functions of access point authorization, configuration and SDN/SDR management.
    R3-C: support control functions of service management, user data connection setup and release, mobility management, accounting management, and location management
    R3-D: support user data forwarding, encryption, tunneling etc.
  R4 between access networks:
    R4-D: support user data forwarding, bi-casting, encryption, etc
    R4-C: Inter-access network coordination and cooperation, fast intra-technology or inter-technology handover.
  R5 between core networks to enable co-use of access networks:
    Inter-operator roaming control interface

## Slide 8: OmniRAN Protocol Stacks
OmniRAN Data Plane Protocol Stack
Medium
Medium
Data Link
Physical
IPv4/6
Application
Data Link
Physical
Data Link
Physical
L1
L2
IPv4/6
Application
Medium
Medium
Data Link
Physical
IP/UDP
L1/L2
IP/UDP
L1/L2
L2
L1
STA
AP
SDN
PDN-GW
APP-SVR
Core
R2
R1
R3
OmniRAN Architecture
AP
STA
SDN
tunnel
tunnel
WLAN
STA
Core
Service
GTP-U
GTP-U
?
?

## Slide 9: OmniRAN Protocol Stacks
OmniRAN Control Plane Protocol Stack
Medium
Medium
Data Link
Physical
C-Signal
Data Link
Physical
Data Link
Physical
Medium
Medium
Data Link
Physical
IP/UDP
L1/L2
IP/UDP
L1/L2
L2
L1
STA
AP
SDN Controller
CTRL
APP-SVR
Core
R2
R1
R3
OmniRAN Architecture
AP
STA
SDN
tunnel
?
?
tunnel
C-Signal
C-Signal
C-Signal
WLAN
STA
Core
Service
GTP-C
GTP-C

## Slide 10: OmniRAN Protocol Stacks
OmniRAN Management Plane Protocol Stack
Medium
Medium
Data Link
Physical
Data Link
Physical
Data Link
Physical
Medium
Medium
Data Link
Physical
IP/UDP
L1/L2
IP/UDP
L1/L2
L2
L1
STA
AP
WAM
MNGR
APP-SVR
Core
R2
R1
R3
OmniRAN Architecture
AP
STA
SDN
tunnel
?
?
tunnel
M-Signal
M-Signal
M-Signal
GTP-?
GTP-?
WLAN
STA
Core
Service

## Slide 11: References
  omniran-13-0096-00-ecsg-approved-par-clean
  omniran-13-0099-00-0000-brief-introduction-into-omniran-p802-1cf
  omniran-13-0067-00-0000-omniran-architecture-suggestions
  omniran-13-0032-05-0000-ieee-802-scope-of-omniran
  omniran-13-0019-02-0000-omniran-wi-fi-hotspot-use-case
  omniran-13-0029-01-0000-sdn-use-case-requirements
  omniran-13-0042-00-0000-orchestration-of-son-features-for-wifi-offloading-using-network-empowerment-mechanisms
  omniran-13-0048-04-0000-omniran-ecsg-results-and-outlook

## Slide 12: Thanks

## Slide 13: Backup
  3GPP 23.402 Interworking Protocol Stack