## Slide 1: SDN-based OmniRAN Use Cases Reference Point Mappings (non-SDN control & data paths)
Terminal
Internet
Core Network(s)
Access Infrastructure
Backhaul
SDN
Controller
Access 3
Access Abstraction
Access Abstraction
Multi-interface Access Abstraction
Access 1
Access 2
Access Abstraction
Backhaul Abstraction
Core
Operator A
Data Path
SDN Ctrl
Core
Operator B
Data Path
SDN Ctrl
R1dA
R1dB
R1d
AAA
OAM
Shared Databases
R2d
R3d
R4
R5

## Slide 2: SDN-based OmniRAN Use Cases Reference Point Mappings (SDN control)
Terminal
Internet
Core Network(s)
Access Infrastructure
Backhaul
SDN
Controller
Access 3
Access Abstraction
Access Abstraction
Multi-interface Access Abstraction
Access 1
Access 2
Access Abstraction
Backhaul Abstraction
Core
Operator A
Data Path
SDN Ctrl
Core
Operator B
Data Path
SDN Ctrl
AAA
OAM
Shared Databases
R3c
R1cA
R1cB
R1c
R2c
R6
R7

## Slide 3: Interface definition
R1: Access link
  R1d: Data-only interface at the link between the terminal and the access point. In case aggregation of interfaces is used, corresponds to the aggregated or logical link.
    R1dA/B: Data-only interface at the link between the terminal and the access point. Corresponds to only one of the interfaces while using interface aggregation.
  R1C: SDN-based configuration/interaction to the terminal and the access point. It does not include configuration of access network but only the 802 link connecting terminal and access point. It includes the configuration of the aggregation interface if it exists.
    R1CA/B: SDN control of link between the terminal and the access point. It may include configuration of interface in the terminal.
R2: User & terminal authentication, subscription & terminal management
  R2d: This is an interface carrying non SDN control frames, it includes session management, interface with AAA services, communication with management platform and external databases such as IEEE 802.19 data base, IEEE 802.21 MIIS or even external databases i.e., possible interaction with ANDSF like databases. This interface can span towards external operators which carry their own processes such as AAA servers.
  R2c: This interface enables the SDN control of the different entities connecting the terminal through R2d. This includes SDN control of the data path followed by R2d and the control interface between the controller and AAA, management platform and databases.

## Slide 4: Functional Requirements
R3: User data connection, service management
  R3d: Data-plane only interface carrying user data from the outer gateway of the access network to a certain core operator network. This network can span from direct connection of the access point WAN interface to the core to a complex heterogeneous transport network (backhaul).
  R3c:SDN control of the links connecting the access network to the core. This reference point/interface does not include the control of the outer gateway of the access network, but includes the data-path control of the user flows.
R4: Inter-access network coordination and cooperation, fast inter-technology handover
  Data-plane only interface carrying user traffic among different access networks.
R5: Inter-operator roaming control interface
  Inter-operator roaming outside access network
    Subscription information exchange between service operators
R6: Control-only interface for the configuration of the access network not including the link between the terminal and the access point. It includes the configuration of the outbound gateway to the backhaul. This interface includes the configuration of the data path used in R4 and the internal data-path of flows within the access network.
R7: Control interface between possible controllers at the different operator cores and the controller of the access network. It is used for the orchestration of multi-tenant access network.

## Slide 5
AN A
AN B
Core B
Data Path
Ctrl
CNS A
Ctrl&ISs
Terminal
R1A
R1B
R2
R3d
R9c
R4
R5
R6d
R6c
R7c
R8c
Ctrl
R3
AN C
R3
R3
R4
PoA
Backhaul
SSP
(AAA,
User Policies,
Etc.)
R3c