## Slide 1
IEEE 802 omniRAN Network Reference Model Amendment |  |  | 
Date: 2014-04-16 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Yonggang Fang | ZTE |  | yfang@ztetx.com
Bo Sun | ZTE |  | sun.bo1@zte.com.cn
He Huang | ZTE |  | Huang.he@zte.com.cn
Notice: This document represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on contributors, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This contribution discusses issues in network reference model of IEEE 802 omniRAN Recommended Practice document, and suggest the amendment for naming convention consistence and reflecting real deployments.

## Slide 2: Current omniRAN Reference Model
Terminal
Interface
R1
Coordination
and
Information
Service
R2
R8c
AN Ctrl
TE Ctrl
Subscription
Service
Core
Network
Interface
R3d
R3s
CNI Ctrl
R3c
Access Network
NA
Backhaul
R6d
R6c
R7c
Terminal
Core
Network
R9c

## Slide 3: Issues
Reference Points
  Inconsistent Naming Convention
    R1 refers to the data path between TEI and NA. It should be changed to R1d according the naming convention.
    R8c refers to the control path between TEI control entity and AN control entity. It should be named as R1c according to the naming convention.
  Missing Reference Points
    Currently R9c represents the external interface between AN control entity and CIS. But CIS may be co-located with AN, or CN depending on the implementation, or operated by 3rd party. Therefore it is necessary to define a new reference point between CIS and CNI controller.
    R6c refers to the control path between AN control entity and NA. However, it misses the case of inter-NA communication. Such communication could be ether indirectly through AN control entity or directly between two NAs (needs a new reference point).
Definition of Network Entities
  It needs to clearly define the functionalities of each network entity in the network reference model section. Referring to [3].

## Slide 4: Proposal of modified NRM
Terminal
Interface
R1d
Coordination
and
Information
Service
R2c
R1c
AN Ctrl
TE Ctrl
Subscription
Service
Core
Network
Interface
R3d
R4c
CNI Ctrl
R3c
Access Network
NA
Backhaul
R6d
R6c
R7c
Terminal
Core
Network
R8c
R9c
R5c

## Slide 5: Proposal of modified NRM
Reference Point Modification
  R1c: Replace R8c with R1c for naming convention consistence
  R1d: Replace R1 with R1d for naming convention consistence.
  R4c: replace R3s with R4c for the reference point between ANC and SS for naming convention consistence
  R5c: The reference point between CNC and SS [4]
  R6c: (no change) the reference point between ANC and NA
  R7c: (no change) the reference point between ANC and BH
  R8c: (new) The reference point between CIS and CNC.
  R9c: (no change) The reference point between ANC and CIS
  Rxc: (TBD) the reference point between NAs (or ANCs)

## Slide 6: Proposal of modified NRM
ANC (AN Ctrl)
  ANC is a logic entity in the IEEE 802 access network, which manages and controls the operation of NAs and backhaul, such as NA setup, provisioning, and/or tear-down.
  ANC could be either a centralized network entity such as Access Controller defined in IETF, or distributed logical functional entity inside of NA.
    As a centralized network entity, ANC uses reference points R6c to control NA and R7c to control the backhaul.
    As the distributed functional entity inside of NA, ANC bridges the communication between Access Networks .
  ANC uses the reference point (R4c) to access Subscription Service (SS) to acquire subscriber’s information during the user authentication, authorization and datapath establishment.
  ANC uses the reference point (R3c) to communicate with CNC for user’s datapath establishment, teardown, or relocation over R3d.

## Slide 7: Proposal of modified NRM
ANC (AN Ctrl)
  ANC uses the reference point (R1c) to communicate with TE for user’s datapath establishment, teardown, or relocation over R1d.
  When operating over the authorized spectrum shared with primary services, the ANC uses reference point (R9c) to access CIS to get the authorized shared access information on the particular location and radio channel, and control the operation of NA over the authorized shared spectrum.
  ANC also control TE’s operation over the authorized shared spectrum through the reference point R1c.

## Slide 8: Proposal of modified NRM
CNC (CNI Ctrl)
  CNC controls the operation of CNI for data path establishment, teardown, or relocation
  CNC uses the reference point (R5c) to access Subscription Service (SS) to acquire subscriber’s information during the user authentication, authorization and datapath establishment.
  CNC uses the reference point (R8c) to access CIS to acquire the authorized shared access information on the particular location and radio channel.
  CNC uses the reference point (R3c) to communicate ANC to control the operation of AN for user’s datapath establishment, teardown, or relocation over the radio access network.

## Slide 9: Proposal of modified NRM
CIS
  CIS provides advanced services such as spectrum management, coexistence, and information services. It has a database to store the information for authorized shared access.
  CIS uses a reference point (R9c or R8c) to communicate the information from these services to the AN control, TE control and CN control entities.
  CIS supports mutual authentication with ANC or CNC.

## Slide 10: References
References
  omniran-14-0083-00-00TG-p802-1cf-network-reference-model
  omniran-15-0013-00-CF00-r9c-reference-point-discussion
  omniran-14-0078-02-CF00-updated-text-for-an-setup.
  omniran-15-0008-00-CF00-nrm-refinements