## Slide 1
Chapter 7.4.1 Revision |  |  | 
Date: [2016-09-27] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Hao Wang | Fujitsu R&D Center | +86-10-59691000 | wangh@cn.fujitsu.com
Su Yi | Fujitsu R&D Center | +86-10-59691000 | yisu@cn.fujitsu.com
Xiaojing Fan | Fujitsu R&D Center | +86-10-59691000 | fanxiaojing@cn.fujitsu.com
Ryuichi Matsukura | Fujitsu/Fujitsu Laboratory | +81-44-754-2667 | r.matsukura@jp.fujitsu.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This presentation proposes one revision on chapter 7.4.1.

## Slide 2: Chapter 7.4.1 Revision
2016-09-27
Hao Wang
Fujitsu R&D Center

## Slide 3: Authenticator in 802.1X and Functions
Authenticator system provides two functions:
      Authentication (control functions provided by ANC)
        Receives authentication information from supplicant (TE) by EAPOL and provides authentication results
        Forwards authentication information to authentication server (SS) by EAPOR and receives authentication results
      Access control (by NA)
Protocol converted at Authenticator (ANC)
Supplicant
Authenticator
Authentication Server

## Slide 4: Comment on 7.4.1
“The port based authentication system consists of a Supplicant System located in the terminal, an Authenticator System located in the node of attachment and an Authentication Server System, which resides in the Subscription Service.” in 7.4.1
Comment: the functions of authenticator system can not be provided solely by NA
  No reference point between NA and SS to support EAPOR protocol
  Detail procedures in 7.4.7 involve both NA and ANC

## Slide 5: Proposed Change
“The port based authentication system consists of a Supplicant System located in the terminal, an Authenticator System located in the node of attachment Access Network and an Authentication Server System, which resides in the Subscription Service.” in 7.4.1

## Slide 6: Questions, Comments