## Slide 1: Thoughts on IEEE 802 network integration with respect to P802.1CF
Max Riegel (Nokia Bell Labs)
2018-11-14

## Slide 2: 802.24 “Network Integration” action item
Action assigned to 802.24 from 802 EC leadership conference in July.
  Discussion on role and positioning of IEEE 802 in standards, especially with respect to 3GPP and the publicity on “5G”
What is meant by Network Integration?
  Does the IEEE 802 architecture provide a unique value to vertical market?
  Is IEEE 802 more suited to deployment in the communication infrastructure of private enterprise, industry, and the individual user? (Compared to 3GPP, which is more oriented towards service providers?)
  The IEEE 802 architecture enables networks that are like Ethernet: Well understood, mature, predictable. A “cleaner” integration of disparate technologies under the common architecture and addressing.
Can we develop a clearer definition and description of this distinction and the value for the user / implementer?
Can this be developed into a white paper?

## Slide 3: Introductory Thoughts
P802.1CF perspective on IEEE 802 Network integration

## Slide 4: The issue … as far as I would understand.
IEEE 802 would like to have a more striking picture of its market position.
  … to better emphasize its relevance in communication infrastructures.

## Slide 5: Why? … as far as I could see it.
‘5G’ of the mobile industry gained overwhelming public awareness.
  Pulling development resources away from other topics into ‘5G’-related projects
  Challenging the established markets of other technologies
Is IEEE 802 challenged by ‘5G’?
  Maybe, but it should keep in mind it made ‘5G’ happen
    Creating huge demand for broadband connectivity through Wi-Fi
    Providing the cost-effective backbone capacity through Ethernet
    Creating the path for MTC and URLLC through 802.15 and TSN
  The technologies and markets are quite distinct
    ‘5G’ is a E2E system designed for the cellular market
    IEEE 802 is a link layer technology, mainly deployed outside of the cellular domain

## Slide 6: What is IEEE 802? A very generic view
IEEE 802 is a set of link layer technologies, not an overarching communication system
Some of the IEEE 802 technologies are extremely successful
  E.g. Ethernet (IEEE 802.3), Wi-Fi (IEEE 802.11)
There is a variety of other solutions
  E.g. IEEE 802.15, IEEE 802.1, IEEE 802.22
Bridging ties the building blocks together
  IEEE 802.1
IEEE 802 does not standardize the system for the market but only building blocks used by others to design systems for the markets.

## Slide 7: What to achieve?
Higher participation?
  More people coming to the meetings?
More projects?
  Bigger organization?
More design-ins?
  Better distribution of knowledge to the engineers?
More public funding and research activities?
  Better cooperation with universities?
… ?

## Slide 8: What is meant by ‘network integration’ ? A P802.1CF perspective
Integration of IEEE 802 components into networks (IEEE 802 networks)?
Integration of IEEE 802 components/ networks into non-IEEE 802 networks?
Both?
P802.1CF provides guidance for both!
  For the IEEE 802 access network only

## Slide 9: P802.1CF Network Model
P802.1CF perspective on IEEE 802 Network integration

## Slide 10: IEEE 802 access network
IEEE 802 access network describes the layer 2 network between terminal and access router implemented through IEEE 802 technologies.
The part of the access infrastructure in scope of P802.1CF is shown through the shaded area of the protocol layer architecture of the data path.
Medium
Medium
Data Link
Physical
Network
Transport
Application
DL
Phy
DL
Phy
Data Link
Physical
Network
Transport
Application
Network
Network
Medium
Medium
Data Link
Physical
Data Link
Physical
DL
Phy
DL
Phy
DL
Phy
DL
Phy
Medium
Backhaul
Node of Attachment
Terminal Interface
Access Router Interface
Scope of specification
Access Network
Access Router
Information Server
Subscription Service
NMS
Terminal

## Slide 11: IEEE 802 Access Network Reference Model
Comprehensive NRM shows highest level of details
NRM represents an abstract view on an access network
  For the purpose to define interfaces
Control interfaces cover only attributes related to IEEE 802
  Protocol details on control interfaces are out of scope

## Slide 12: P802.1CF is able to cover the control of Time Sensitive Networks
P802.1CF access network represents the bridged connectivity between end stations
Access Network Control (ANC) provides centralized network configuration for TSN sessions
  CNC is contained in ANC
R8, R9, and ANC provide means to process User/Network Configuration Info

## Slide 13: Network softwarization Building networks through software
P802.1CF provides model for network virtualization of IEEE 802 access networks
Allows for realization of several separate networks on a common infrastructure
Virtualization establishes separate control instances for each of the networks
BTW: VLANs provide separate datapaths under a common control

## Slide 14: Network integration with external networks
IEEE 802 Access Network
External Network
Access Router
Access Network
Terminal
Terminal Interface
R1
Coordination and Information Service
R2
R10
R8
Access Network Control
TEC
Subscription
Service
Access Router Interface
R3
R4
ARC
R9
R12
Network Management System
R11
NA
Backhaul
R6
R5
R7
P802.1CF provides a model for interfacing with external networks.

## Slide 15: Deployment Examples
P802.1CF perspective on IEEE 802 Network integration

## Slide 16: Wi-Fi Router
Wi-Fi Router may be the most common example of IEEE 802 access network
Generic schematic of Wi-Fi Router
Micro Controller
RAM
FPROM
IEEE 802.11 Interface
Ethernet Bridge
ETH PHY
ETH PHY
ETH PHY
ETH PHY
ETH PHY
LAN
LAN
LAN
LAN
WAN
IEEE 802.11 Interface
…
eth1
eth0

## Slide 17: Wi-Fi Router
Mapping of Wi-Fi router to NRM
NA
LAN-WAN Gateway
Access Network
Terminal
Terminal Interface
R1
Coordination and Information Service
R2
R10
R8
Access Network Control
TEC
Subscription
Service
Access Router Interface
R3
R4
ARC
R9
R12
Network Management System
R11
NA (802.11)
Backhaul
R6
R5
R7
Terminal Interface
‘WAN’
NA
NA
NA
NA
(802.3)
R6
R1
WLAN Router
R8
R1
TEC
R2
‘LAN’

## Slide 18: Enterprise Network
Schematic example of Enterprise Network with multiple segments (VLANs)
Network
Management
Directory
Internet
other sites
WLAN-Ctrl
WAN Router
Firewall+VPN Gateway

## Slide 19: Enterprise Network
Access portion of Enterprise Networks with multiple segments (VLANs) can be represented through NRM
AR
AN
TE
TEI
R1
R1
CIS
R10
R8
ANC
TEC
SS
R3
R4
ARC
R12
NMS
R11
NA
BH
R6
R5
R7
Network
Management
Directory
Internet
other sites
WLAN-Ctrl
WAN Router
Firewall+VPN Gateway
R9
R2

## Slide 20: Industrial Network
Schematic example of Industrial Network
Network
Management
Directory
WLAN-Ctrl

## Slide 21: Industrial Network
AR
AN
TE
TEI
R1
R1
R1
R1
CIS
R2
R10
R8
ANC
TEC
SS
R3
R4
ARC
R12
NMS
NA
BH
R6
R7
Network
Management
Directory
WLAN-Ctrl
The access portion of an Industrial Network can be represented through the NRM

## Slide 22: Virtualized residential Wi-Fi access for IoT
Multiple Wi-Fi accesses through ‘multi SSID’ configuration at CPE and traffic separation on the broadband access
Network virtualization allows for multiple separate access infrastructures on a common infrastructure.
CPE

## Slide 23: Virtualized residential Wi-Fi access for IoT
While not all of the residential broadband access infrastructure is defined by IEEE 802, its functional model is well applicable.
P802.1CF provides architecture and functional model of virtualized IEEE 802 access network, which can be applied to Wi-Fi.

## Slide 24: Fog Computing
Fog computing deploys Cloud-technologies at the edge of the access network.
Fog computing provides considerable operational and economic benefits for IoT and communication services.
Network
Management
Fog control and orchestration
WLAN-Ctrl
Cloud
Fog

## Slide 25: Fog Computing
Fog computing extends data-center networking concepts into the wide-area access network.
The access portion of the Fog computing networks can be represented through NRM.
AR
AN
TE
TEI
R1
R1
R1
R1
CIS
R2
R10
R8
ANC
TEC
SS
R3
R4
ARC
R12
NMS
NA
BH
R6
R7
Network
Management
Fog control and orchestration
WLAN-Ctrl
Cloud
Fog
R5
R11

## Slide 26: Conclusion
P802.1CF perspective on IEEE 802 Network integration

## Slide 27: Conclusion
The intention and the scope of the IEEE 802 network integration action item requires further clarifications and discussions
  Better understanding of intended outcome needed
P802.1CF has rich material to support the action item.
BTW: It is planned to forward P802.1CF to REVCOM before next IEEE 802 meeting.